Features

- Compliant with Bluetooth v2.0 Specification with EDR (Enhanced Data Rate) support

- Backward compatible with Bluetooth v1.1 and v1.2 devices

- Up to 3Mbps access data rate and low power consumption

- Compatible with Windows 98SE/ME/2000/XP & MCE (Media Center Edition) Operating Systems

- Built-in 128-bit encryption of secured data communications

- Enable computers to connect Bluetooth-enabled devices such as printers, headset, audio/video, basic images, PDAs, and mobile phone.

- Compliant with Class II Bluetooth Operations

- Communicates wirelessly up to 10 meters (32.8 ft.) (depends on the environment)

- Trouble free Plug & Play installation

- 2-Year Warranty

Specifications

| Hardware |
| --- |
| Standards | Class II Bluetooth v2.0 with EDR Backward Compatible with Bluetooth v1.1 & V1.2 USB 1.1 |
| Antenna | PCB Antenna |
| Supported OS | Windows 98SE/ME/2000/XP, MCE |
| Operating Voltage | 5V (USB Bus-Powered) |
| Power Consumption | 170mA (Max) |
| Temperature | Operation: 0( C~ 55( C (32( F~132( F), Storage: -20( C~ 55(C (-4(F~132(F) |
| Humidity | 95% (Max) |
| Dimensions | 47 x 15 x 10 mm (1.85 x 0.59 x 0.39 in.) |
| Weights | 9 g (0.3 oz.) |
| Certification | CE, FCC |
| Bluetooth |  |
| Frequency | 2.4 ~ 2.4835 GHz |
| Module Technique | GFSK (Gaussian Frequency Shift Keying). π/4 DQPSK, 8DPSK |
| Encryption | 64/128-bit Encryption |
| Profile Support | Bluetooth Imaging, Human Interface Device, Printer, Audio Gateway, Headset, PIM Synchronization, Fax, File Transfer, PIM Item Transfer, Dial-up Networking, Network Access, Bluetooth Serial Port |
| RF Output Power | 3dBm (typical) |
| Receiving Sensitivity | - 80dBm ( max) |
| Data Rate | Up to 3Mbps |
| Date Range | Up to 10m (32.8 ft.) Depends on Environment |

Package Contents				Related Products

- TBW-101UB 					- TBW-102UB

- Multi-Language Quick Installation Guide	- TBW-104UB

- Driver CD-ROM				- TBW-105UB

- USB Cable

To order please call: 888-326-6061 • Sales: sales@trendware.com

Support: support@trendnet.com • Tech Support Hotline: 866-845-3673

Official Site: www.trendnet.com

# Text boxes

TBW-101UB (Version v3.0R)

Bluetooth USB Adapter

Venture into the wireless realm with TRENDnet Bluetooth technology.  Enhance your PCs with Bluetooth peripherals.  Unclutter your workspace with TBW-101UB Bluetooth wireless technology.

New Implements

- Chipset ( Broadcom BCM2045B3

- EDR support

- Software ( Widcomm