Features

Wireless

- Wi-Fi Compliant with IEEE 802.11g and IEEE 802.11b Standards

- Supports Ad-Hoc (Peer-to-Peer) Mode or Infrastructure (AP-Client) Mode

- Dynamic Data Rate Scaling at 54, 48, 36, 24, 18, 12, 9 and 6Mbps for 802.11g

- Dynamic Data Rate Scaling at 11, 5.5, 2 and 1Mbps for 802.11b

- Supports 64/128/256-bit WEP and WPA Encryptions

- Range of 100 meters indoor, 400 meters outdoor (depends on the environment)

Bluetooth

- Compliant with Bluetooth v1.2 and Class 2 Operation

- Fully Bluetooth v1.2 BQB Qualified

- Compatible with Microsoft HID Devices

- Support up to 7 active and 8 parked slaves

- Bluetooth Range of up to 10 meters

General

- Uses 2.4 GHz Frequency Band, which Complies with Worldwide Requirements

- Compatible with Windows 2000/XP (SP1/SP2)

- Simple User Setup & Diagnostics Utilities

- 3-Year Warranty

Specifications

| Hardware |
| --- |
| Interface | USB 2.0, 1.1 Compliant, Bluetooth 1.2 Class 2 |
| Dimensions (LxWxH) | 100 x 30 x 15 mm (3.9 x 1.2 x 0.6 inches) |
| Weight | 32g (1 oz.) |
| Temperature | Operating: 0( ~ 60( C (32( ~ 140( F) Storage: -20( ~ 70( C (-4( ~ 158( F) |
| Humidity | 5% ~ 95%max (Non-condensing) |
| Safety Emissions | FCC, CE |
| Wireless |
| Module Technique | 802.11b: CCK (11 and 5.5Mbps), DQPSK (2Mbps), DBPSK (1Mbps) 802.11g: OFDM |
| Frequency | 2.412 ~ 2.484 GHz |
| Data Rate (auto fallback) | 802.11b: 11Mbps, 5.5Mbps, 2Mbps, and 1Mbps 802.11g: 54Mbps, 48Mbps, 36Mbps, 24Mbps, 18Mbps, 12Mbps, 9Mbps and 6Mbps |
| Transmit Power | 802.11b: 16dBm ± 2dBm; 802.11g: 13dBm ± 2dBm 802.11g: 15dBm @ 54Mbps |
| Receiving Sensitivity | 802.11b: < -70dBm @PER < 10%, All Rate 802.11g: < -70dBm @PER < 8%, All Rate |
| Encryption | 64/128/256-bit WEP, AES-CCM, and TKIP |
| Channels | 1~11 (US), 1~13 (EU) |
| Bluetooth |
| Module Technique | Gaussian Frequency Shift Keying (GFSK) |
| Frequency | 2.400 ~ 2.483.5 GHz |
| Data Rate | Up to 723Kbps |
| Range | Up to 10 meters |
| Encryption | 128-bit Encryption |

Package Contents				Related Products

-TBW-103UB					- TEW-421PC		- TBW-101UB

- Utility & Driver CD-ROM			- TEW-423PI		- TBW-102UB

- Multi-Language Quick Installation Guide	- TEW-430APB

- TEW-432BRP

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

## Sales: sales@trendnet.com • Support: techsupport@trendnet.com

Tech Support Hotline: (888)777-1550

www.trendnet.com

# Text boxes

802.11g Wireless & Bluetooth Combo USB Adapter

The 54Mbps 802.11g Wireless USB 2.0 & Bluetooth Combo Adapter simultaneously provides Bluetooth and Wi-Fi connections, allowing you to concurrently link to Wi-Fi Internet hotspots and Bluetooth devices.  Experience the power of downloading ring tones, iTunes, or digital pictures from a wireless Internet connection and transfer the same files seamlessly into your Bluetooth enabled phone.  The external antenna can be adjusted easily to improve signal strength gain and transmission.

#### TBW-103UB