Features

- Built-in 1 Parallel (DB 25) and 2 USB 2.0 (Type A) Printer Ports

- Compliant with USB 2.0 High-Speed Printing

- One RJ-45 10/100Mbps Auto-MDIX Fast Ethernet Port

- Supports Email Printing and FTP Printing

- Includes LPR Program for Windows 98/ME TCP/IP Printing

- Supports IPP Printing for Windows 2000/XP

- Supports Universal Plug and Play (UPnP) for Windows XP/2003

- Supports Windows Graphical Device Interface (GDI) Printers

- Supports second HTTP port for Remote Web Configuration and IPP Printing

- Supports Mac 10.2 “Rendezvous” Zero-Configuration Function

- Latest MIB-II (RFC 1213) for SNMP Standard Management

- IP Assignment Support for DHCP, BOOTP and RARP

- Includes Windows-Based Administrative Program and Web-Based Configuration

- Built-in Flash Memory for Easy Firmware Upgrade and Configuration File Save & Restore

- Printing Access Control/Display and Email Notification for Printer Error Messages

- 5-Years Warranty

*Mac Systems are only compatible with Post-Script printers

Specifications

| Hardware |
| --- |
| Standards | IEEE 802.3 10Base-T IEEE 802.3u 100Base-TX |
| Printer Interface | 2 x USB 2.0 Type A Port 1 x Parallel DB25 (Female) Port |
| LAN Port | 10/100Mbps Auto-Negotiation UTP/STP RJ-45 Port |
| CPU | RDC R2880 100MHz |
| SDRAM | 8MByte |
| Flash ROM | 2MByte |
| LED | Power, LAN, USB1, USB2, LPT |
| Transport Protocol | TCP/IP, SMB, NetBEUI, AppleTalk |
| TCP/IP Protocol Supported | BOOTP, SNMP, Telnet, TFTP, FTP, LPD, RARP, DHCP, IPP |
| OS Support | Windows 95/98(SE)/ME/NT/2000/XP/2003 Netware 5.x NDPS LPR Remote Printing (TCP/IP) HP-UX Unix, Sun OS, Solaris, SCO Unix, AIX Unixware, Linux & Mac OS 9 or higher. |
| Management | PS Utility, PS Monitor or Web-Browser Configuration |
| Power | 5V DC 2.5A External Power Adapter |
| Dimensions | 206 x 122 x 34mm (8.1 x 4.8 x 1.3 in.) |
| Weight | 289 g ( 10.2oz.) |
| Temperature | Operating: 0(~50(C (32(~122(F) Storage: -25(~55(C (-13(~131(F) |
| Humidity | 10%~90% (non-condensing) |
| Certification | CE, FCC |

Package Contents						   Related Products

- TE100-P21					                              - TE100-P1P

- Multi-Language Installation Guide                              		    - TE100-P1U

- Utility CD-ROM				                              - TEW-P21G

- Power Adapter (5V DC, 2.5A)

To order please call: 888-326-6061 •  Sales: sales@trendnet.com

Support: support@trendnet.com • Technical Support: 310-626-6252

Official Site: www.trendnet.com

# Text boxes

New Implements:

- New Housing

- Support GDI Printers

10/100Mbps Multi-Port Print Server

TRENDnet TE100-P21 is a Fast Ethernet print server that transforms a stand-alone USB or Parallel printer into a shared network printer. The TE100-P21 is compatible with 10Mbps or 100Mbps Ethernet network and it has two USB 2.0 and one Parallel printer port. Network professionals can easily manage the print server using Web Browser and utilize the TE100-P21 to promote productivity in a workgroup environment with low equipment cost.

Network Solution for TE100-P21

TE100-P21 H/W: 2.1