Features

- PCMCIA CardBus 68-pin Connector Type II Card

- 32-Bit Bus-Mastering Data Transfer

- 10/100Mbps Data Rate Auto-Negotiation Operation

- Built-in Transmit 4Kbytes RAM Data Buffers

- Supports Full-Duplex Mode Doubles Network Data Rate to 20/200Mbps

- Integrated RJ-45 XpressPort for Dongle/Coupler-Free Connection

- Supports Windows 98SE/ME/2000/XP

- Ultra Low Power Consumption

- Single Shielded RJ-45 Connector & UTP/STP Cabling Supported

- Compatible with Extensive Notebook Models

- Supports Hot Swap and Plug & Play

- 5-Years Warranty

Specifications

| Hardware |
| --- |
| Standards | IEEE 802.3 10BASE-T Ethernet IEEE 802.3u 100BASE-TX Fast Ethernet ANSI/IEEE 802.3 Auto-Negotiation PCMCIA 2.x 32-Bit CardBus |
| Network Media | Ethernet: UTP Cat. 3, 4, 5, EIA/TIA-568 100-ohm STP Fast Ethernet: UTP Cat. 5, EIA/TIA-568 100-ohm STP |
| Data Rate | Ethernet: 10Mbps/20Mbps (Half/Full-Duplex) Fast Ethernet: 100Mbps/200Mbps (Half/Full-Duplex) |
| Protocol | CSMA/CD |
| Interface | 32-Bit CardBus Type II |
| Dimension | 120 x 53 x 3mm (4.7 x 2 x 0.1 inches) |
| Power Consumption | 3.3V DC |
| Diagnostic LED | 10M Link/Activity 100M Link/Activity |
| Supported Drivers | Windows 98SE/ME/NT4.0/2000/XP Novell NetWare Server 3.21, 4.1x, 5.0 Novell Netware ODI for DOS / ODI Client 32 Packet Driver, NDIS 2.0 |
| Temperature | Operating: 0° ~ 40° C (32° ~ 104° F) Storage: -10° ~ 70° C (14° ~ 158° F) |
| Humidity | Operating: 10%~90% (Non-Condensing) Storage: 5%~90% (Non-Condensing) |
| Safety Emissions | FCC, CE |

##### TOP REASONS THE TE100-PCBUSR IS A LASTING TREND

| User Friendly | Just plug the card into your workstation and it’s ready to go! |
| --- | --- |
| Flexibility | Supports all major Network Operating Systems |
| Compatibility | Compatible with extensive notebook computers |
| Low Cost | Integrated Xpress Port reduces user down time and eliminates dongle/jack replacement |

Package Contents				Related Products

- TE100-PCBUSR				- TEG-PCBUSR

- Multi-Language Quick Installation Guide	- TE100-PCIWN

- Driver CD-ROM

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

## Sales: sales@trendware.com • Support: techsupport@trendware.com

Tech Support Hotline: (310)626-6252

Official Site: www.TRENDNET.com

# Text boxes

### 10/100Mbps CardBus PC Card

TE100-PCBUSR gears with leading 32-bit bus architecture and full-duplex capabilities, which liberates high-speed network performance by providing a smooth connection to both 10/100Mbps Ethernet environments. This card is the ultimate solution for the CardBus equipped addition. Its auto-negotiation feature also configures to meet any kind of network card. It also guarantees easy installation and extra low power consumption with power-down mode and broad compatibility.

#### TE100-PCBUSR (v2.0R)

Network Solution for TE100-PCBUSR