FEATURES

- Complies with IEEE 802.3, IEEE 802.3μ, and IEEE 802.3x standards

- Plug-and-Play (PnP) for auto-configuration

- Supports 32-bit PCI bus master specification Rev 2.1/2.2

- Supports full-duplex mode that doubles the data rate up to 20Mbps/200Mbps

- Supports full-duplex flow control (IEEE 802.3x)

- Supports 10/100Mbps N-way auto-negotiation

- Easy-to-view LED indicators

- Built-in FIFO buffers reduces overhead of memory transfers

- Compatible with all popular operating systems

- Complies with PC99 standard

- Advanced power saving mode when LAN function or wake-up function is not used

- Supports Magic Packet™ remote wake-up method – Wake-on-LAN

- Supports ACPI, PCI power management

- 5-years warranty

TREND SPEC’S

| Standards: | IEEE 802.3 10Base-T, IEEE 802.3μ 100Base-TX, ANSI/IEEE 802.3 N-way auto-negotiation, IEEE 802.3x full-duplex flow control |
| --- | --- |
| Protocol: | CSMA/CD |
| Network Media: | Ethernet: UTP CAT 3, 4, 5 EIA/TIA-568 100-ohm screened twisted pair (STP), Fast Ethernet: UTP CAT 5, EIA/TIA-568 100-ohm screened twisted pair (STP) |
| Data Transfer Rate: | 10/100Mbps (Half-duplex), 20/200Mbps (Full-duplex) |
| Diagnostic LEDs: | Link, Activity |
| Network Drivers: | Novell NetWare ODI, NDIS, SCO UNIX, LAN Manager, Windows 95/98/2000/NT, Windows for Workgroups, Packet Driver, LAN server, Warp server, Linux and many others |
| Operating Temp.: | 0( to 50( C (32( to 122( F) |
| Storage Temp.: | -20( to 70( C (-4( to 158( F) |
| Operating Humidity: | 10 % to 90 % non-condensing |
| Storage Humidity: | 5 % to 90 % non-condensing |
| Certifications: | FCC, CE, VCCI-II |

TOP REASONS THE TE100-PCIWA IS A LASTING TREND

Performance:	Operates in the 32-bit bus master mode, delivering throughputs as multi-megabits per second with little stress on the host’s CPU.

Flexibility: 	With the Wake-on-LAN capability, network administrators can remotely wake up computers equipped with the adapters.

Migration: 	Half-/full-duplex auto-detect both 10Base-T and 100Base-TX modes.  Make the adapter ideal for high-speed server when increased to 200Mbps network speed.

Cost-Effectiveness:	Complying with PC99 standard and power saving mode, TRENDnet PCI PnP adapter is the perfect choice for cost-effective and high-bandwidth workgroup networking.

TE100-PCIWA	32-bit PCI 10/100Mbps N-way Fast Ethernet Card

with ACPI Wake-on-LAN

TE100-PCIWN		32-bit PCI 10/100Mbps N-way Fast Ethernet Card

TE-16PCTplus		16-bit ISA PnP Ethernet Card with BNC + RJ-45 Connectors

TE-16PTplus		16-bit ISA PnP Ethernet Card with RJ-45 Connector

TE-PCIWplus		32-bit PCI PnP Ethernet Card with BNC + RJ-45 Connectors

TE-PCIWTplus		32-bit PCI PnP Ethernet Card with RJ-45 Connector

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

Sales: sales@trendware.com • Support: Techsupport@trendware.com

# Text boxes

TE100-PCIWA

PRODUCT

INFORMATION

PC Card

Network Solution

32-bit PCI 10/100Mbps N-way

Fast Ethernet Card with Wake-on-LAN

The TE100-PCIWA, a 10/100Mbps Fast Ethernet Plug-and-Play PCI adapter with ACPI, utilizes the latest chipset technology and provides easy installation. It senses 10Mbps or 100Mbps (20Mbps or 200Mbps in full-duplex mode) automatically and connects to Ethernet/Fast Ethernet network with single RJ-45 connector. Supporting PCI v2.1 and 2.2 standards, it works with current and new PCI v2.2 standards with 3.3V bus voltage. The Wake-on-LAN functions to remotely wake up the workstation. With TRENDnet adapter, your desktop will turn into a high-bandwidth graphic/multimedia workstation or a power server running at full-duplex speed.

TE100-PCIWA