Features

- 8 10/100Mbps Auto-Negotiation, Auto-MDIX Fast Ethernet RJ-45 ports

- Compliant with IEEE 802.3 / IEEE 802.3u standards

- IEEE 802.3x Flow Control support

- Provide 1K MAC address entries

- Compliant with Windows, Linux, and Mac Operating Systems.

- Store-and-Forward Switching method

- Non-blocking Architecture

- Diagnostic LEDs

- Plug & Play

- 5-Year Warranty

Specifications

| Hardware |
| --- |
| Standards | IEEE 802.3 10Base-T IEEE 802.3u 100Base-TX IEEE 802.3x Flow Control |
| Network Media | Ethernet: UTP/STP Cat. 3,4,5, EIA/TIA-568 100-ohm Fast Ethernet: UTP/STP Cat. 5. 5E, EIA/TIA-568 100-ohm |
| Data Rate | Ethernet: 10Mbps/20Mbps (Half/Full-Duplex) Fast Ethernet: 100Mbps/200Mbps (Half/Full-Duplex) |
| Switch Fabric | 1.8Gbps Forwarding Capacity |
| Topology | Star |
| Interface | 8 10/100Mbps Auto-MDIX RJ-45 Ports |
| Filtering Table | 1K Entries per device |
| Power Consumption | 2.8 watts (max) |
| Diagnostic LED | Power, Link/ACT, 100Mbps |
| Power Adapter | Switching Power 5V DC 800mA or Linear Power 7.5V DC 1A / 9V DC 600mA |
| Dimension | 154 x 110 x 33mm (6 x 4.3 x 1.3 inches) |
| Weight | 225g (8oz.) |
| Temperature | Operating: 0° ~ 50° C (32° ~ 122° F) |
| Humidity | 10%~90% (Non-Condensing) |
| Certification | CE, FCC |

Package Contents						Related Products

- TE100-S8							- TE100-PCIWN

- Multi-Language Quick Installation Guide			- TE100-PCBUSR

- Power Adapter (5V DC, 800mA)

To order please call: 888-326-6061 • Sales: sales@trendnet.com

Support: support@trendnet.com • Technical Support: 866-845-3673

Official Site: www.trendnet.com

# Text boxes

8-Port 10/100Mbps Fast Ethernet Switch

TE100-S8 is an Auto-MDIX switch designed specifically to boost network performance by eliminating network congestions and unnecessary network traffics.  Each port on the Switch provides dedicated bandwidth and can negotiate between 10/100Mbps network speeds and half/full duplex modes. Plug-N-Play provides cost-effective and high performance solutions.

#### TE100-S8 (v1.0R)