Features

- 16 x 10/100/1000Mbps Auto-Negotiation and Auto-MDIX Gigabit Ports

- 2 x 1000Base-SX/LX Mini-GBIC Slots for Optional Mini-GBIC Modules

- Full Wire-Speed Non-Blocking Reception and Transmission

- Store and Forward Switching Method

- Extensive Diagnostic LED’s on the Front Panel

- IEEE 802.3x Flow Control for Full/Half-Duplex Mode; Back Pressure Flow Control for Half-Duplex Mode

- Supports 802.1Q VLAN and 802.1p Priority Queues

- Supports Trunking (max 6 groups, 8 ports per group) and Port Mirroring

- Supports Jumbo Frame Packets Transfer (Max Size up to 10240bytes)

- Integrated Address Look-Up Engine, Supports 8K Absolute MAC addresses

- Supports 512Kbytes RMA for Data Buffering

- Port Setting Function, Users can set each Port’s Availability, Speed, Duplex Mode, and Flow Control

- Easy Configuration via Web browser

- Standard 19” (1U) Rack Mount Size

- 5-Year Warranty

# Specifications

| Hardware |
| --- |
| Standards | IEEE 802.3 10Base-T ; IEEE 802.3μ 100Base-TX IEEE 802.3ab 1000Base-T ; IEEE 802.3z 1000Base-SX/LX (Mini-GBIC) IEEE 802.3x Full Duplex Flow Control |
| Protocol | CSMA/CD |
| Transmission Method | Store-and-Forward |
| Interface | 16 10/100/1000Mbps Auto-MDIX RJ45 Ports 2 1000Base-SX/LX Mini-GBIC Slots (share with Gigabit ports 15 and16) |
| Network Media | Ethernet: 2-pair UTP Cat. 3, 4, 5, up to 10Mbps Fast Ethernet: 2-pair UTP Cat. 5, up to 100Mbps Gigabit: 4-pair UTP Cat. 5, 5E, 6, up to 1000Mbps |
| Data Transfer Rate | 10Mbps: 10/20Mbps (Half/Full Duplex) 100Mbps: 100/200Mbps (Half/Full Duplex) 1000Mbps: 2000Mbps (Full Duplex) |
| Data RAM Buffers | 512KBytes per device |
| Filtering Address Table | 8K entries per device |
| Switch Fabric | 32Gbps Forwarding Capacity |
| Diagnostic LEDs | Per Unit: Power, System Per Copper Gigabit Port: Link/ACT, 1000M, 100M Per Mini-GBIC Port: Link/ACT, 1000M |
| Power Supply | 100 ~ 240VAC 50/60Hz, Internal Universal Switching Power |
| Power Consumption | 30 Watts (Max) |
| Dimension | 440mm x 210mm x 44mm (17.3 x 8.3 x 1.73 inches) |
| Weight | 3Kg (6.6 lb) |
| Temperature | Operating: 0(C ~ 40(C (32(F ~ 104(F); Storage: -10(C to 70(C (14(F to 158(F) |
| Humidity | Operating: 10 % ~ 90 % (non-condensing); Storage: 5 % ~ 90 %(non-condensing) |
| Certification | CE, FCC |

Package Contents                  			Related Product	Optional Mini-GBIC Modules

- TEG-160WS					- TEG-PCBUSR		- TEG-MGBSX

- Multi-Language Quick Installation Guide	- TEG-PCITXR		- TEG-MGBS10

- CD-ROM (Utility/UG)				- TEG-240WS		- TEG-MGBS40

- Rack Mount Kit				- TEG-448WS		- TEG-MGBS80

- Power Cord								- TEG-MGBS10D35

- TEG-MGBS40D35

To order please call: 888-326-6061

20675 Manhattan Place, Torrance, CA 90501 • (310) 961-5500 • Fax: (310) 961-5511

### Sales: sales@trendnet.com • Support: techsupport@trendnet.com

### Official Site: www.TRENDNET.com

# Text boxes

TEG-160WS (h/w: C1.0R)

16-port Gigabit Web Smart Switch

w/ Mini-GBIC Slots

TEG-160WS 16-Port 10/100/1000Mbps Web Smart Switch is the ideal Switch for network segmenting.  TEG-160WS supports web browser configuration; Network Administrator can use web browser to configure port speed, port-based VLAN and QoS, and also monitor each port’s status which provides simple migration, scalability, and flexibility to handle new applications and data types. TEG-160WS is powerful and easy-to-use in reducing unnecessary broadcast traffic and enhance network security.

New Implements

- Add 2 Mini-GBIC Slots

- Jumbo Frame Support