Features

- 16 x 10/100/1000Mbps Auto-Negotiation and Auto-MDIX Gigabit Ports

- Full/Half Duplex Transfer Mode for 10/100Mbps Ports

- Full Duplex Transfer Mode for Gigabit Ports

- Full Wire-Speed Non-Blocking Reception and Transmission

- Store and Forward Switching Method

- 512K bytes RAM data buffer and 8K entries MAC address table

- Extensive diagnostic LED’s on the front panel

- IEEE 802.3x flow control for full-duplex mode; Back Pressure flow control for half-duplex mode

- Proprietary Windows Based Management/Monitoring Utility (similar to SNMP Trap)

- Port-Based VLAN and Port-Based IEEE 802.1p QoS (High/Normal)

- Supports Trunking and Port Mirroring

- Port Setting function, users can set each port’s availability, speed, duplex mode, and flow control

- Easy configuration via Web browser

- Standard 19” (1U) Rack Mount Size

- 5-Year Warranty

# Specifications

| Hardware |
| --- |
| Standards | IEEE 802.3 10Base-T ; IEEE 802.3μ 100Base-TX IEEE 802.3ab 1000Base-T ; IEEE 802.3x Full Duplex Flow Control |
| Protocol | CSMA/CD |
| Transmission Method | Store-and-Forward |
| Interface | 16 10/100/1000Mbps Auto-MDIX RJ45 Ports |
| Network Media | Ethernet: 2-pair UTP Cat. 3, 4, 5, up to 10Mbps Fast Ethernet: 2-pair UTP Cat. 5, up to 100Mbps Gigabit: 4-pair UTP Cat. 5, 5E, 6, up to 1000Mbps |
| Data Transfer Rate | 10Mbps: 10/20Mbps (Half/Full Duplex) 100Mbps: 100/200Mbps (Half/Full Duplex) 1000Mbps: 2000Mbps (Full Duplex) |
| Data RAM Buffers | 512KBytes per device |
| Filtering Address Table | 8K entries per device |
| Switch Fabric | 32Gbps Forwarding Capacity |
| Diagnostic LEDs | Per Unit: Power, System, Per Port (RJ-45): Link/Activity, 100Mbps |
| Power Supply | 100 ~ 240VAC 50/60Hz, Internal Universal Switching Power |
| Power Consumption | 23 Watts (Max) |
| Dimension | 440mm x 210mm x 44mm (17.3” x 8.3” x 1.73”) |
| Weight | 3 Kg (6.6 lb) |
| Temperature | Operating: 0(C ~ 40(C (32(F ~ 104(F) Storage: -10(C to 70(C (14(F to 158(F) |
| Humidity | Operating: 10 % ~ 90 % (non-condensing) Storage: 5 % ~ 90 %(non-condensing) |
| Emissions | FCC, CE |

Package Contents                  				Related Product

- TEG-160WS						- TEG-PCBUSR

- Multi-Language Quick Installation Guide		- TEG-PCITXR

- CD-ROM (Utility/UG)					- TEG-224WSplus

- Rack Mount Kit					- TEG-2248WS

- Power Cord

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

### Sales: sales@trendnet.com • Support: techsupport@trendnet.com

### Official Site: www.TRENDNET.com

# Text boxes

TEG-160WS (ver. B4.0R)

16-port 10/100/1000Mbps Gigabit

Web Smart Switch

TEG-160WS 16-Port 10/100/1000Mbps Web-Based Smart Switch is the ideal Switch for network segmenting.  It has 16 10/100/1000Mbps Auto-Sensing and Auto-MDIX ports for easy installation. TEG-160WS supports web browser configuration; Network Administrator can use web browser to configure port speed, port-based VLAN and QoS, and also monitor each port’s status which provides simple migration, scalability, and flexibility to handle new applications and data types. TEG-160WS is powerful and easy-to-use in reducing unnecessary broadcast traffic and enhance network security.