Features

- Compliant with IEEE 802.3u 100Base-FX

- 8 x 100Base-FX Multi-Mode SC Type Fiber Port (TEG-S3M8FX)

- 8 x 100Base-FX Single-Mode SC Type Fiber Port (TEG-S3M8S15)

- Optional Modules for TEG-S3000i (Layer 2 Managed Chassis Switch)

- 5-Year Warranty

Specifications

| Hardware |
| --- |
| Standards | IEEE 802.3u 100Base-FX IEEE 802.3x flow control |
| Interface | 8 100FX (Multi Mode or Single Mode) SC-Type Ports |
| Network Media | 50/125 um or 62.5/125um for Multi-Mode Fiber Optic, Up to 2km 8/125um or 9/125um for Single-Mode Fiber Optic, Up to 15km |
| Switch Architecture | Store/Forward |
| LED | Link, Activity |
| Connector | SC |
| Protocol | CSMA/CD |
| Wavelength | 1310nm |
| Range | Single-Mode: 30km Multi-Mode: 2km |
| Dimensions | 126 x 46 x 35mm (5.0 x 1.8 x 1.4 in.) |
| Weight | 88g (3.1oz.) |
| Temperature | Operating: 0(~45(C (32(~113(F) Storage: -10(~70(C (14(~158(F) |
| Humidity | 10%~90% (non-condensing) |
| Certification | CE, FCC |

Package Contents				Related Products

- TEG-S3M8FX/TEG-S3M8S15			- TEG-S3000i		- TEG-S3M2MG

- TEG-S3M8FX		- TEG-S3M11CF

- TEG-S3M8S15	- TEG-S3M2CG

To order please call: 888-326-6061 • Sales: sales@trendnet.com

Support:  techsupport@trendnet.com • Tech Support Hot Line: 888-777-1550

Official Site: www.trendnet.com

# Text boxes

TEG-S3M8S15

8-Port 100Base-FX SC Type Single-Mode Fiber Module

TEG-S3M8FX

8-Port 100Base-FX SC Type Multi-Mode Fiber Module