FEATURES

- Complies with IEEE 802.11b 2.4GHz DSSS 11Mbps Wireless Standard

- Supports AP, Station Bridge (AP Client), AP Router, and AP Bridge modes

- DHCP Server and Client modes

- Build-in 10dBi High Gain Flat Panel Antenna

- Provides wireless security with 64-bit/128-bit Wired Equivalent Privacy (WEP) and Access Control List

- Adjustable radio output power (10, 13, 16, or 20 dBm)

- Signal Strength LED indicators (AP Client Mode only)

- Local/Remote Management via SSH, SNMP (Bridge MIB, Ethernet MIB, MIB II, Private MIB), Telnet and Web Browser (HTTPS)

- Firewall (with Port Forwarding) provides security in Router Mode

- Includes many useful “System Tools” such as, Connected Client List, Loopback Test (determines bandwidth of a particular end point), Site Survey, Wireless Traffic Monitor, Firmware Upgrade, Device Reboot, and Device Reset.

- IP66 compliant weatherproofed housing with built-In heater for outdoor applications

- Power-Over-Ethernet (POE) Support

- 3-Year Warranty

TREND SPEC’S

### Wireless LAN Interface

Standards: 		IEEE 802.11b Wireless LAN (DSSS 2.412 ~ 2.4835 GHz ISM Band)

Protocol:		CSMA/CA with ACK

Channels:	14 Channels with pre-programmed domain selections to support worldwide requirements

Data Rate:	11Mbps, 5.5Mbps, 2Mbps, and 1Mbps (auto-fallback)

Operating Mode:	Default: AP, AP Router or Bridge modes

Optional (requires firmware upload): Station Bridge (AP Client) and

Station Router (AP Client with Router)

Security:	64-bit & 128-bit WEP Encryption, Access Control List (using MAC Address)

Antenna:	Flat Panel 10dBi, 45( Vertical/Horizontal pattern

RSSI Indicators:	10 LEDs for Receiver Signal Strength Indication in Station (AP Client) Mode

Transmit Power:	20 ± 1dBm. (adjustable to 10, 13, or 16 dBm. Chinese domain is fixed to 10 dBm)

Receive Sensitivity:	11Mbps: -82dBm @10–5 BER CCK, 5.5Mbps: -84dBm @10–5 BER CCK,

& Modulation Tech.	1Mbps: -90dBm @10–5 BER DBPSK

#### Wired LAN Interface

Standards:	IEEE 802.3 (10Base-T) and IEEE 802.3u (100Base-TX)

Port:	10/100Mbps, Half-/Full-duplex Auto-Negotiation

LED Indicator:	Power, Wireless, LAN

Power Supply:	100~230VAC to 5VDC 1.5A Power Adapter, 3W max. with Power-Over-Ethernet

Dimensions:	180 x 160 x 58 mm (7.1 x 6.3 x 2.3 inches)

Weight:	approx. 1.1Kg (2.95 lb) with mounting hardware

Operating Temperature:	-20(C ~ 65(C (-4(F ~ 149(F)

Humidity:	95% (non-condensing)

Certifications:	FCC, CE

TOP REASONS THE TEW-212APBO IS A LASTING TREND

Integration Friendly:	Supports Ethernet/Fast Ethernet Network and Web Browser configuration for fast and easy configuration. Power-Over-Ethernet unit supplies the electricity over Ethernet cable.

Performance:	Effective built-in 10dBi directional antenna for wireless inter-building network bridging or Internet “Hot-Spot” applications.

Flexible:	Works as stand-alone AP, AP Bridge, AP Client, or AP Router.

Security:	Provides 64-bit or 128-bit WEP Encryption, Access Control List, and Firewall.

TEW-212APBO	11Mbps High Gain Outdoor Wireless AP Bridge with Router

TEW-310APBX	11/22Mbps Wireless Access Point + Bridge (with detachable antennas)

TEW-311BRP	11/22Mbps Wireless AP Router with 4-Port Switch

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

## Sales: sales@trendware.com • Support: techsupport@trendware.com	ss04102003

# Text boxes

11Mbps High Gain Outdoor Wireless AP Bridge with Router

TRENDnet’s TEW-212APBO Wireless Access Point Bridge with Router performs Access Point, Access Point Router, and Wireless Bridging functions all in one device.  TEW-212APBO is compliant with IEEE 802.11b and supports 64/128-bit WEP encryption. The unit’s housing is weatherproof for indoors/outdoors applications to increase wireless communication distance, giving the network flexibility to extend between buildings. TEW-212APBO is easily accessible and configurable via FTP, SNMP, Telnet or Web-Based management tools. With TRENDnet’s TEW-212APBO, users can connect to Ethernet/Fast Ethernet LAN at home or office to access network resources or share an Internet connection with coverage up to 3.5 Km.

TEW-212APBO

11Mbps Wireless Network Solution

Product Information