## FEATURES

- IEEE 802.11b Wireless, IEEE 802.3 Fast Ethernet Standards Compliant

- 4-Port 10/100Mbps Auto-Sensing, Auto-MDIX Switch for Sharing Internet Connection for up to

253 Users

- 1-Port 10/100Mbps Auto-MDIX WAN Port

- Dynamic Data Rate Shift at 11, 5.5, 2 and 1Mbps

- Supports 64/128-bit Wired Equivalent Privacy (WEP)

- Supports Cable/xDSL Modem (Dynamic IP, Static IP, PPPoE, PPTP)

- Supports NAT Firewall Protection

- Supports Virtual Server (10 entry) and DMZ (1 entry)

- Internet Access with IP Address (10 entry). MAC Address and Special Application Filter.

- Supports UPnP (Universal Plug & Play)

- Easy Configuration Using Web Browser

- Flash Memory for Firmware Upgrade

- Dual Detachable 2dBi Antennas with Female Reverse SMA Connetors

- Distance Coverage 50 to 100 meters indoor, 100 to 500 meters outdoor

- 3-Year Warranty

## TREND SPEC’S

Standards: 		IEEE 802.11b Wireless LAN, IEEE 802.3, IEEE 802.3u and

ANSI/IEEE 802.3 Auto-Negotiation

Protocols:	DHCP (Client and Server), TCP/IP, NAT, PPPoE, PPTP, SNTP and HTTP

Module Technique:	Direct Sequence Spread Spectrum (DSSS), CCK, DQPSK, DBPSK

Channel:	1~11 Channel

Wireless Data Rate:	11Mbps, 5.5Mbps, 2Mbps, and 1Mbps

Frequency Range:	2.4 ~ 2.497 GHz

Security:	64/128-bit WEP Encryption

Antenna:	2 x Detachable 2dBi Antenna with Reverse SMA connector

Output Power:	13 dBm (max.)

Receiving Sensitivity:	11Mbps: 10-5 BER @ -83 dBm (min.).

2Mbps: 10-5BER @ -84 dBm (min.)

Local Port:	4 UTP/STP 10/100Mbps Auto-MDIX ports

WAN Port:	1 UTP/STP 10/100Mbps Auto-MDIX port

Throughput:	83Mbps (LAN to WAN), 5.05Mbps (LAN to WLAN)

Flash Memory/RAM:	8M/8M

LED Indicators:	Unit: Power, System

LAN Port: LINK/ACT, Speed

WAN Port: LINK/ACT, Speed

WLAN: ACT

Power:	7V DC, 1A External Power Adapter

Dimensions:	171 x 100 x 34 mm (6.73 x 3.93 x 1.3 inch), without Antenna

Weight:	appr. 272g. ( 9.6oz.)

Temperature:	Operating: 0(~ 55(C (32(F~131(F)

Storage: -25( ~ 70(C (-13(F~158(F)

Humidity:	10% ~ 95% RH (non-condensing)

Certification:	FCC, CE

TOP REASONS THE TEW-231BRP IS THE LASTING TREND

Easy Integration: Broadband Router, Access Point, and 4-port 10/100Mbps Switch all

in one unit, share your broadband Internet connection with 802.11b wireless and wired 	Ethernet Clients.

Cost-Effectiveness: Saves on-line charges and spaces.

Security: NAT firewall protection keeps hackers out. 64/128-bit WEP and MAC Address

Access Control protects AP from unwanted wireless clients.

Performance: Experience the high speed Internet access while reducing network traffic.

Product Information

TEW-231BRP	Cable/DSL 802.11b 11Mbps Wireless Router

TEW-226PC	11Mbps 802.11b Wireless PC Card

TEW-228PI	11Mbps 802.11b Wireless PCI Adapter

TEW-222CF	11Mbps 802.11b Compact Flash Adapter

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

Sales: sales@trendware.com • Support: techsupport@trendware.com

www.TRENDNET.com

# Text boxes

TEW-231BRP

Cable/DSL 802.11b 11Mbps Wireless Router

TRENDnet’s TEW-231BRP 11Mbps 802.11b Wireless Router delivers wireless internet access for your home or small office. It includes a Wireless Access Point, Internet Router, and 4-Port 10/100Mbps Switch all in one. Now you can share a Cable or DSL connection with multiple wired or wireless users! Protect your network from outside intruders with a Network Address Translation (NAT) firewall and 128-bit WEP encryption for wireless data transfer. Also, limit access to undesirable content by controlling web access via URL or Time/Date. Setting up the unit is effortless with a Web Browser Configuration tool and UPnP support. Cut the wires and move freely with TRENDnet’s 802.11b wireless products.

Network Solution for

TEW-231BRP