Features

- Wi-Fi Compliant with IEEE 802.11g and IEEE 802.11b Standards

- Detects IEEE 802.11b, and 802.11g HotSpots

- Connects to IEEE 802.11b or 802.11g Wi-Fi Devices

- Supports Ad-Hoc (Peer-to-Peer) Mode or Infrastructure (AP-Client) Mode

- Dynamic Data Rate Scaling at 54, 48, 36, 24, 18, 12, 9 and 6Mbps for 802.11g

- Dynamic Data Rate Scaling at 11, 5.5, 2 and 1Mbps for 802.11b

- Built-in Rechargeable Li-on Battery (Automatically charge when connected to the USB port) and Back Light Support

- Hotspot Finder displays SSID, Channel, Security Enable/Disable and Signal Strength information

- Supports Custom Search by Signal Strength, SSID or Encryption

- Maximum Reliability, Throughput and Connectivity with Automatic Data Rate Switching

- Supports WEP, WPA/WPA2 and WPA-PSK/WPA2-PSK Encryption without Performance Degradation

- Low Interference and High Susceptibility Guarantee Reliable Performance

- Compatible with Windows 98SE/ME2000/XP/2003 Server

- Range of 35~100 meters indoor, 100~300 meters outdoor (depends on the environment)

- Simple User Setup & Diagnostics Utilities

- 3-Year Warranty

Specifications

| Hardware |
| --- |
| Interface | USB 2.0, 1.1 Compliant |
| LCD / LED | 96 x 32 pixels, Back Light / PWR, ACT |
| Control | Power On/Off, Scan, Next |
| Rechargable Battery | 180mAh |
| Power Consumption | 280mA |
| Dimensions (LxWxH) | 97.3 x 28.6 x 14 mm (3.8 x 1.1 x 0.6 inches) |
| Weight | 35g (1.2 oz.) |
| Temperature | Operating: 0( ~ 40( C (32( ~ 104( F) Storage: -20( ~ 70( C (-4( ~ 158( F) |
| Humidity | 10% ~ 90%max (Non-condensing) |
| Safety Emissions | FCC, CE |
| Wireless |
| Module Technique | 802.11b: CCK (11 and 5.5Mbps), DQPSK (2Mbps), DBPSK (1Mbps) 802.11g: OFDM |
| Frequency | 2.412 ~ 2.484 GHz |
| Media Access Protocol | CSMA/CA |
| Data Rate (auto fallback) | 802.11b: 11Mbps, 5.5Mbps, 2Mbps, and 1Mbps 802.11g: 54Mbps, 48Mbps, 36Mbps, 24Mbps, 18Mbps, 12Mbps, 9Mbps and 6Mbps |
| Transmit Power | 15dBm ± 2dBm |
| Receiving Sensitivity | 802.11b: -87dBm @ 11Mbps 802.11g: -72dBm @ 54Mbps |
| Encryption | 64/128-bit WEP (Hex / Passphrase), WPA/WPA2 (AES/TKIP) WPA-PSK/WPA2-PSK, 802.1x |
| Channels | 1~11 (US), 1~13 (EU), Japan (11b :1~14, 11g: 1~13) |

Package Contents				Related Products

- TEW-429UB					- TEW-421PC

- Utility & Driver CD-ROM			- TEW-423PI

- Multi-Language Quick Installation Guide	- TEW-430APB

- TEW-432BRP

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

## Sales: sales@trendware.com • Support: techsupport@trendware.com

Tech Support Hotline: (310)626-6252

Official Site: www.TRENDNET.com

# Text boxes

# 54Mbps 802.11g Wireless USB 2.0 Adapter

# with HotSpot Detector

The 802.11g Wireless USB 2.0 adapter combines features from Wi-Fi detectors and standard 802.11g wireless adapter to deliver the perfect solution for mobile users.  It has built-in LCD display helps you determine an access point’s security scheme (WPA/WPA2, WEP), signal strength, and wireless standard (802.11b or 802.11g) without turning on your laptop!

New Implements

- Add Back Light for LCD Display

- RoHS Compliant

- Add WPA2 / WPA2-PSK

#### TEW-429UB (c2.0R)