Features

- Wi-Fi Compliant with IEEE 802.11g and 802.11b Wireless Standards

- Uses 2.4 GHz Frequency Band, which Complies with Worldwide

- Smart Antenna Design and support up to 108Mbps in Super G mode

- Supports Ad-Hoc (Peer-to-Peer) Mode or Infrastructure Mode

- Dynamic Data Rate Scaling at 54, 48, 36, 24, 18, 12, 9 and 6Mbps for 802.11g

- Dynamic Data Rate Scaling at 11, 5.5, 2 and 1Mbps for 802.11b

- Maximum Reliability, Throughput and Connectivity with Automatic Data Rate Switching

- Compliant with Windows 98SE/ME/2000/XP/2003

- Supports WEP and WPA/WPA2 Encryptions

- Supports Wireless Multimedia Enhancements Quality of Service (QoS)

- Low Interference and High Susceptibility Guarantee Reliable Performance

- Low Power Consumption and Easy Configurations

- Range of 35~100 meters indoor, 100~300 meters outdoor (depends on the environment)

- Simple User Setup & Diagnostics Utilities

- 3-Year Warranty

Specifications

| Hardware |
| --- |
| Interface | USB 2.0, 1.1, 1.0 Compliant |
| Standards | IEEE 802.11b and IEEE 802.11g |
| LED Indicator | Link |
| Power Consumption | 450mA @5V DC |
| Supported OS | Windows 98SE/ME/2000/XP/2003 |
| Dimensions (LxWxH) | 115 x 80 x 33 mm (4.5 x 3.1 x 1.3 inches) |
| Weight | 92 g (3.25 oz.) |
| Temperature | Operating: 0( ~ 40( C (32( ~ 104( F) Storage: -20( ~ 70( C (4( ~ 158( F) |
| Humidity | 10% ~ 95% max (Non-condensing) |
| Safety Emissions | FCC, CE |
| Wireless |
| Module Technique | 802.11b: CCK (11 and 5.5Mbps), DQPSK (2Mbps), DBPSK (1Mbps) 802.11g: OFDM with BRPSK, QPSK and 16/64-QAM sub-carrier modulations |
| Frequency | 2.412 to 2.484 GHz (Industrial Scientific Medical Band) |
| Media Access Protocol | CSMA/CA |
| Antenna | 3 x 2dbi Antennas |
| Data Rate (auto fallback) | 802.11b: 11Mbps, 5.5Mbps, 2Mbps, and 1Mbps 802.11g: 54Mbps, 48Mbps, 36Mbps, 24Mbps, 18Mbps, 12Mbps, 9Mbps and 6Mbps **6Mbps for 802.11g using USB 1.1 or 1.0 Connection Super G : 108Mbps |
| Output Power | 20dBm (typical) @ 802.11b 14dBm (typical) @ 802.11g |
| Receiving Sensitivity | 54Mbps 10% PER @ -73 dBm (typical) 11Mbps 8% PER @ -88 dBm (typical) |
| Security | 64/128/152-bit WEP (Hex), WPA/WPA2(AES/TKIP) WPA-PSK/WPA2-PSK, 802.1x |
| Channels | 1~11 (US), 1~13 (EU) |

Package Contents					Related Products

- TEW-604UB 					- TEW-601PC

- Quick Installation Guide				- TEW-603PI

- Utility & Driver CD-ROM				- TEW-610APB

- USB 2.0 Cable (1.5m/4.9ft.)				- TEW-611BRP

# To order please call: 1-888-326-6061 (USA)

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

## Sales: sales@trendware.com • Support: techsupport@trendware.com

Tech Support Hotline: (310)626-6252

## www.TRENDNET.com

# Text boxes

108Mbps 802.11g Smart Wireless

USB 2.0 Adapter

TEW-604UB 802.11g Wireless USB 2.0 Adapter brings together the convenience of USB 2.0 and the high speed of 802.11g, allowing you to easily connect to 802.11g networks at speeds of up to 108Mbps. The USB 2.0 interface facilitates a hassle-free Plug-and-Play installation, and 128-bit WEP Encryption provides robust network security. The TEW-604UB is a feature-rich yet convenient way to go wireless.

TEW-604UB (v1.0R)