Features

- Compatible with 2.4GHz 802.11b/g or 5GHz 802.11a wireless devices.

- Works with any brand of wireless devices with reverse SMA male connector

- Serves as an indoor omni relocation antenna

- Enhances wireless coverage and improve signal transmission and reception

- Adjustable antenna face can tile up to 180° and rotate up to 360° for optimal performance.

- No configuration or installation software required

- 3-Year Warranty

Specifications

| Hardware |  |  |  |
| --- | --- | --- | --- |
| Frequency Range | 802.11a: 4.9 ~ 5.875GHz 802.11b/g: 2.4 ~ 2.5GHz | Power Handling | 2W (cw) |
|  |  | Impedance | 50 Ohms |
| Gain | 802.11a:7dBi 802.11b/g:5dBi | Connector | Reverse SMA Female |
|  |  | Dimension | 217 x 28 x14mm (8.5 x 1.1 x 0.55in.) |
| VSWR | 2.0:1 |  |  |
| Polarization | Linear, vertical | Weight | 41g (1.4oz.) |
| HPBW/ Horizontal | 360° | Temperature | -10°C ~ 55°C (14°F ~ 131°F) |
| HPBW/ Vertical | 802.11a:25° 802.11b/g: 35° |  |  |
|  |  | Humidity | 95% at 25°C |

Radiation Patterns

Package Content 						Related Product

- TEW-AI75O						- TEW-AI75OB

- Multi-Language User’s Guide				- TEW-AI86D

- TEW-AI86DB

To order please call: 888-326-6061; Sales: sales@trendnet.com

Support: support@trendnet.com; Tech Support Hotline: 888-777-1550

Official Site: www.trendnet.com

# Text boxes

TEW-AI75O

Dual-band 11a/g 7/5dBi Indoor Omni Antenna

TEW-AI75O Omni Antenna provides more power and greater range for your wireless network. As an optional antenna for your IEEE 802.11b/g 2.4GHz or 802.11a 5GHz wireless network equipment, TEW-AI75O will significantly improve signal strength and quality.  TEW-AI75O will work with any brand of devices with reverse SMA male connector!

* This dBi gain does not factor cable loss. Performance estimations are for typical use; range will vary with site conditions.

Antenna Solution with TEW-AI75O