Features

- Compatible with 2.4GHz 802.11b/g or 5GHz 802.11a wireless devices

- Detachable antenna base allows high gain antenna to be optionally connected to Wi-Fi device, avoiding cable loss/attenuation

- Magnetic base allows convenient and optimal relocation to wall or any metallic surface

- Serves as an indoor directional relocation antenna

- Enhances wireless coverage and improve signal transmission and reception

- Adjustable antenna face can tilt up to 180° and rotate up to 360° angel for optimal performance

- Easy-to-install wall and ceiling mount

- No configuration or installation software required

- 3-Year Warranty

Specifications

| Hardware |  |  |  |
| --- | --- | --- | --- |
| Frequency Range | 802.11a: 4.9 ~ 5.8GHz 802.11b/g: 2.4 ~ 2.5GHz | Connector | Reverse SMA Female |
|  |  | cable length | 100cm (3.3ft.) |
| Gain | 802.11a: 8dBi 802.11b/g: 6dBi | Dimension | Antenna: 128x85x15 (5.04x3.35x0.59in) Base: 80x58x28mm(3.15x2.28x1.1in) |
| VSWR | 2.0:1 |  |  |
| Polarization | Linear, Vertical |  |  |
| HPBW/ Horizontal | 802.11a: 50° 802.11b/g: 75° | Weight | Antenna: 51g(1.8oz.) Base: 82g(2.9oz.) |
| HPBW/ Vertical | 802.11a: 60° 802.11b/g: 70° | Temperature | -10°C ~ 55°C (14°F ~ 131°F) |
| Power Handling | 2W (cw) | Humidity | 95% at 25°C |
| Impedance | 50Ohms |  |  |

Radiation Patterns

Package Content 						Related Product

- TEW-AI86DB						- TEW-AI86D

- Mounting Kit						- TEW-AI75O

- Multi-Language User’s Guide				- TEW-AI75OB

To order please call: 888-326-6061; Sales: sales@trendnet.com

Support: support@trendnet.com; Tech Support Hotline: 888-777-1550

Official Site: www.trendnet.com

# Text boxes

TEW-AI86DB

Dual-Band 802.11a/g 8/6dBi 
Indoor Directional Antenna with Mounting Base

TRENDnet’s TEW-AI86DB Indoor Directional Antenna provides more power and greater range for your wireless network. As an optional antenna for your IEEE 802.11b/g 2.4GHz or 802.11a 5GHz wireless network equipment, TEW-AI86DB will significantly improve signal strength and quality.  TEW-AI86DB will work with any brand of device with Reverse SMA Male Connector!

* This dBi gain does not factor cable loss. Performance estimations are for typical use; range will vary with site conditions.

* This Figure does not include cable loss

Antenna Solution with TEW-AI86DB