TREND SPEC’S

| Frequency range: | 2400 MHz ~ 2500MHz |
| --- | --- |
| Gain: | 8.0 dBi |
| VSWR: | 2.0 : 1 Max. |
| Polarization: | Linear, Vertical |
| HPBW/horizontal | 360 o |
| HPBW/vertical | 15 o |
| Power Handling: | 50 W (cw) |
| Impedance: | 50 Ohms |
| Connector Lead Cable: | RG-58/u, 27 cm (10.6”) |
| Connector Type: | N-Type female |
| Antenna Cable Type: | 2 Meters (6 ft.) HDF-200 (TEW-2000F), N-Type male to Reverse SMA female. Attenuation: 1.1 dB |
| Survival Wind Speed: | 180 Km/h (112 Miles/h) |
| Temperature: | -40 oC ~ 80 oC (-40 oF ~ 176 oF) |
| Humidity: | 100% @ 25 oC (77 oF) |
| Lightning Protection: | DC ground |
| Radome Color: | Gray-white |
| Radome Material: | Fiberglass |
| Housing Material: | PCB micro stripe |
| Weight: | 400g (14 oz.) |
| Dimensions: | 520 x 62 x 79.5 mm (20.47 x 3.13 x 2.44 inches) |
| Warranty: | 3-Year |
| Optional Antenna Cable: | 8 Meters (26 ft.) HDF-200 (Model: TEW-8000F) Attenuation: 4.5 dB |

NOTE: For optimal results in extending your wireless range with

wireless antenna installations, we recommended that you consult

a professional installer for site survey, safety precautions, and

proper installation.

Antenna Dimensions

Network Solution with TEW-OA08OK

TEW-OA08OK	8dBi Omni Directional Outdoor Antenna Kit for IEEE 802.11b/g 2.4GHz Band

TEW-OA14DK	14dBi Directional Outdoor Antenna for IEEE 802.11b/g 2.4GHz Band

TEW-OA24D	24dBi Directional Outdoor Antenna for IEEE 802.11b/g 2.4GHz Band

TEW-IA04O    	4dBi Omni Directional Indoor Antenna for IEEE 802.11b/g 2.4GHz Band

TEW-IA06D    	6dBi Directional Indoor Antenna for IEEE 802.11b/g 2.4GHz Band

FOR MORE INFORMATION CALL 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

sales@trendware.com • techsupport@trendware.com		ss10282003

# Text boxes

## TEW-OA08OK

PRODUCT

INFORMATION

8dBi Omni-Directional Outdoor Antenna Kit

TRENDnet's TEW-OA08OK Outdoor Omni Directional Antenna Kit increases the coverage area of your wireless network. As an optional antenna for your 2.4GHz IEEE 802.11b and 802.11g wireless network equipments, you can install it indoor or outdoor to extend the coverage area. The antenna can simply be mounted on the wall or on a pole. This antenna kit comes antenna, metal bracket, hardware, and 2 meters (6 ft.) antenna cable. You can install the kit on any brand’s 2.4GHz wireless devices with Reverse SMA Male antenna connector. Unleash the power of your wireless products with TRENDnet's TEW-OA08OK antenna.

Pattern

Vertical

Horizontal

(mm / inches)