TREND SPEC’S

| Frequency range: | 2400 MHz ~ 2500MHz |
| --- | --- |
| Gain: | 14.0 dBi |
| VSWR: | 1.4 : 1 Max. |
| Polarization: | Vertical linear |
| 3dB beamwidth / H-plane: | 30 o |
| 3dB beamwidth / E-plane: | 30 o |
| Front to Back Ratio: | 15 dB |
| Down tilt: | 0o |
| Power Handling: | 50 W (cw) |
| Impedance: | 50 Ohms |
| Connector Lead Cable: | RG-58/u, 27cm (10.6”) |
| Connector Type: | N-Type, female |
| Antenna Cable: | 50 Ohms with male N-Type and female Reverse SMA connectors |
| Survival Wind Speed: | 180 Km/h (112 Miles/h) |
| Temperature: | -30 oC ~ 80 oC (-22 oF ~ 176 oF) |
| Humidity: | 100% @ 25 oC (77 oF) |
| Lightning Protection: | DC ground |
| Radome color: | Gray-white |
| Radome material: | ABS/UV resistant, Fire retardant |
| Housing material: | Galvanized Steel, Fire retardant |
| Weight: | 0.825 Kg (1.82 lb) |
| Dimensions: | 240 x 240 x 69.5 mm (9.5 x 9.5 x 2.7 inches) |
| Warranty: | 3 Years |

Positioning Your Antenna

You may need to position your antenna higher up or to the left or right for better reception.

Network Solution with TEW-OA14DK

TEW-OA14DK	14dBi Directional Outdoor Antenna for 2.4 GHz ISM Band wireless device with RG-58 Cable (TEW-2000F) and mounting kit

TEW-IA04O    	4dBi Omni Antenna (indoor) for IEEE 802.11b 2.4GHz ISM Band

TEW-IA06D    	6dBi Directional Antenna (indoor) for IEEE 802.11b 2.4 GHz ISM Band

TEW-223PI	11Mbps Wireless PCI Adapter for Desktop

TEW-210APB	11Mbps Wireless Access Point with Bridge and Client feature

FOR MORE INFORMATION CALL 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

sales@trendware.com • techsupport@trendware.com	ss07112003

# Text boxes

## TEW-OA14DK

PRODUCT

INFORMATION

TEW-OA14DK 14dBi Outdoor Directional Antenna with 6ft. (2 meters) Low Loss Antenna Cable and Mounting Kit

TRENDnet’s TEW-OA14DK Outdoor Directional Antenna provides long distance point-to-point connection for your wireless network. As an optional antenna for your IEEE 802.11b 2.4GHz 11/22Mbps wireless network equipments, you can install it outdoor for connecting network up to 8 Km away, or install it in the building to blast through obstructions. Designed for TEW-203PI, TEW-210APB, TEW-211BRP and TEW-303PI, you can simply mount the antenna indoor on the ceiling, wall, or outdoor tower.  Unleash the power of your wireless products with TRENDnet’s TEW-OA14DK antenna.  Will work with any brand with Reverse SMA Male Connector!

Pattern

NOTE: For optimal results in extending your wireless range with wireless antenna installations, we recommended that you consult a professional installer for site survey, safety precautions, and proper installation.