#### Features

- Compliant with IEEE 802.3 10Base-T and IEEE 802.3u 100Base-TX, 100Base-FX standards

- One 10/100Base-TX Auto-Negotiation, Auto-MDIX RJ-45 port

- One 100Base-FX multi-mode SC-type Fiber port

- Supports LLCF (Link Loss Carry Forward)

- Provides Dip switches to set: UTP (Auto Negotiation/Full Duplex), Fiber (Half Duplex/Full Duplex) , LLCF (Enable/Disable), Mode (Pure Mode/ Switch Mode)

- 802.3x flow control for 10/100Base-TX port

- Diagnostic LEDs

- Plug & Play, Hot Swappable

- Optional 19” Fiber Converter Chassis (TFC-1000) holds up to 10 Media Converters

- 5-Year Warranty

#### Specifications

|  | Media | Wavelength | Power Output (dBm) | Sensitivity (dB) | Power Budget (dBm) | Distance |
| --- | --- | --- | --- | --- | --- | --- |
| 50/125µm | MMF | 1310nm (1270nm~1380nm) | -23.5 | -31 | 7.5 | 2km |
| 62.5/125µm |  |  | -20 | -31 | 11 |  |

| Hardware |
| --- |
| Standard | IEEE 802.3 10Base-T IEEE 802.3u 100Base-TX, 100Base-FX |
| Network Media | 10Base-T: UTP/STP Cat. 3, 4, 5, EIA/TIA-568 100-ohm 100Base-TX: UTP/STP Cat. 5, EIA/TIA-568 100-ohm 100Base-FX: 50/125μm or 62.5/125μm Multi-Mode Duplex SC-Type Fiber Cable, up to 2km |
| Protocol | CSMA/CD |
| Frame Packet Size | 64 to 1600 Bytes |
| Ports | 1 x 10/100Base-TX RJ-45 Port 1 x 100Base-FX Multi-Mode SC-Type Fiber Port |
| Dip Switch | Dip Switch 1: ON: TX Port Fully Duplex OFF: TX Port Auto- Negotiation Dip Switch 2: ON: FX Port Half Duplex OFF: FX Port Full Duplex Dip Switch 3: ON: LLCF Enable OFF: LLCF Disable Dip Switch 4: ON: Pure Converter Mode OFF: Switch Converter Mode * After changing the DIP Switch settings, power cycle the Fiber converter. |
| Transfer Rate | 100Mbps (Half/Full Duplex) |
| Diagnostic LED | Per Device: Power Per port (TX): 100Mbps, Link/Activity, Full Duplex/Collision (FX): Link/Activity, Full Duplex/Collision |
| Power Adapter | 9V DC, 700mA External Power Adapter |
| Power Consumption | 2.7 Watts (max) |
| Dimensions | 85 x 125 x 25mm (3.35 x 4.92 x 0.98in.) |
| Weight | 300g (10.6oz.) |
| Temperature | Operating : 0( C ~ 45( C (32( F ~ 113( F) Storage : -40( C ~ 70( C (-40(F ~ 158( F) |
| Humidity | 5% ~ 90% RH |
| Certification | CE, FCC |

To order please call: 888-326-6061 • Sales: sales@trendnet.com
Support: support@trendnet.com • Tech Support Hotline: (866)845-3673

www.trendnet.com

# Text boxes

TFC-210MSC (v1.0R)

_

10/100Base-TX to 100Base-FX Fiber 
Multi-Mode SC-Type Fiber Converter

This Fiber Converter transforms 10/100Base-TX UTP/STP media to 100Base-FX multi-mode media. The 10/100Base-TX port supports auto-negotiation and auto-MDIX.  Designed to connect up to 2KM, the converters are the perfect Fast Ethernet, multi-mode solution.