FEATURES

- Small form factor integrates into mobile and handheld platforms

- Complies with CF+ & CompactFlash Rev. 1.4

- Xpress Port design, with integrated RJ11 phone connector into the card. No moving parts to break and no media coupler to lose

- Designed for Windows CE handheld devices to connect to Internet

- High performance 16C550A compatible UART

- Digital line protection design, prevent burned out when connecting to high-current digital PABX

- Plug and Play device for easy installation and configuration

- “Hot Swap” card insertion and removal

- LED indicators display adapter and connection status

- Low power consumption and automatic sleep mode

- Auto-step downward compatibility for connection

- 3-Year warranty

TREND SPEC’S

Card Type: 	CF+ & CompactFlash Rev. 1.4

Modem Standards:	V.90, K56Flex, V.34+, V.34, V.32bis, V.32, V.23, V.22bis, V.22/Bell 212A, V.21/Bell 103, Hays Compatible AT Command Set

Fax Standards:	Group 3, V.29, V.27ter, V.21 Channel 2, V.17, EIA Class 1 Commands

Error Control:	V.42, MNP Class 2 to 4

Data Compression:	V.42bis, MNP Class 5

Receive Sensitivity:	-40 (±) dBm

Transmit Level:	Permissive –10 (±) dBm

Diagnostic:	Power-Up Self Test, Local Analog Loopback Test, Local Digital Loopback Test, Remote Digital Loopback Test

Dialing Methods:	DTMF Tone and Rotary Pulse

Operation Modes:	Asynchronous Full Duplex, Automatic and Manual Answer

Flow Control:	Hardware CTS/RTS, Software XON/XOFF

LED Indicators:	Power, Link, Data

Power Consumption:	3.3V; Sleep Mode: 18.5 mA; Operating Mode: 186 mA (max.)

Dimensions:	83 x 43 x 16 mm (3.27 x 1.69 x 0.63 inch)

Operating Temp.:	0( ~ 70( C (32( ~ 158( F)

Storage Temp.:	-20( ~ 90( C (-4( ~ 194( F)

Humidity:	10% ~ 90% (no-condensing)

Certification:	FCC Class B, CE

TOP REASONS THE TFM-CF56 IS A LASTING TREND

User Friendly: 	Easy installation with “Hot-Swap” card insertion and removal.

Economical:	Xpress Port design that integrates RJ11 phone connector into the card. No moving parts to break and no media coupler to lose.

Flexible:	Supports most modem/Fax standards and negotiates connection speed between 300bps and 56Kbps.

Performance:	Surfs the Internet with speed up to 56Kbps

TFM-CF56		CompactFlash 56K Fax Modem Card

TE100-CF56		CompactFlash 10/100Mbps Fast Ethernet Adapter

TEW-CF56		CompactFlash 11Mbps Wireless LAN Adapter

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

Sales: sales@trendware.com • Support: techsupport@trendware.com

# Text boxes

Product Information

TFM-CF56

CompactFlash 56K Fax Modem Card

TRENDnet’s TFM-CF56 CompactFlash 56K Fax Modem Card is the latest in communication innovation.  Designed with an integrated RJ-11 connector for telephone line connection, this CompactFlash Fax Modem is the easiest and fastest way to connect to the Internet.  Designed for Pocket PC / Windows CE-base palm sized hand-held PCs, you can just insert the card and then dial-up to ISP for accessing Internet and e-mails. With the “Hot Swap” option, TRENDnet’s TFM-CF56 provides easy installation and configuration for your dial-up applications.

## Network Solution for

TFM-CF56