Features

- Use one keyboard, monitor, and mouse to control two computers

- PS/2 Keyboard/Mouse emulation

- 2-Port KVM switch in compact size design

- Supports Microsoft Intellimouse, Optical Mouse, Logitech Net Mouse and more

- Supports High Video Quality, up to 1920 x 1440 with 200MHz resolution

- Supports Dos, Windows 98(SE)/ME/2000/XP/2003 Server, Unix, Linux and more

- Hot-Plug feature, add PC or remove the connected PC for maintenance without powering down the KVM Switch or other PC’s

- Auto-Scan Mode for monitoring PC’s.

- Hot-Key & Push Buttons for PC selection

- Keyboard status restored when switching between PCs

- LED display for easy status monitoring

- Beeping sound for port switching confirming

- 2-Year Warranty

Specifications

| Hardware |
| --- |
| Management | 2 Computers |
| Cable Interface (all male, cable not included) | To KVM: 1 x PS/2 Mouse 6-pin Mini Din 1 x PS/2 Keyboard 6-pin Mini Din 1 x VGA/SVGA HDB 15-pin | To PC: 1 x PS/2 Mouse 6-pin Mini Din 1 x PS/2 Keyboard 6-pin Mini Din 1 x VGA/SVGA HDB 15-pin |
| Console & PC Connectors (all female) | Mouse: PS/2 6-pin Mini Din Keyboard: PS/2 6-pin Mini Din Monitor: VGA/SVGA HDB 15-pin |
| Port Selection | Push Button and Hot-Key Commands |
| Auto-Scan Interval | 4 seconds |
| Power Type | Bus-Powered |
| Power Supply | 9V DC, 500mA Optional External Power Adapter (not included) |
| Dimensions | 113 x 84 x 31mm (4.45 x 3.31 x 1.22in.) |
| Weight | 155g (5.5oz.) |
| Temperature | Operating: 0(C ~ 40(C (32(F ~104(F) Storage: -20(C ~ 60(C (-4(F ~140(F) |
| Humidity | 0%~80%, Non-Condensing |
| Certifications | CE, FCC |

Package Contents							Related Products

- TK-200								- TK-208K

- Multi-Language Quick Installation Guide		                          - TK-408K

- TK-400K

To order please call: 888-326-6061 • Sales: sales@trendnet.com 
Support: support@trendnet.com  • Tech Support Hotline: 866-845-3673

Official Site: www.trendnet.com

# Text boxes

# 2-Port PS/2 KVM Switch

The TK-200 2-Port KVM Switch lets you manage two PCs with just one keyboard, monitor and mouse.  Switch between two PC's with a simple press of a button!  With its Hot-Plug, Auto-Scan, Audible Feedback, and Hot-Key operations, the TK-200 is the perfect choice for managing multiple PCs.

#### TK-200 (B1.1R)

KVM Solution for TK-200