FEATURES

- Support Microsoft Intellimouse, Microsoft Intellimouse Explorer, Logitech NetMouse, Optical Mouse, or other fully compatible MS Mouse.

- PS/2 Keyboard/Mouse emulation

- Support DOS, Windows 3.x/95/98/ME/NT/2000/XP, Netware, Unix, Linux, and more

- Very high video quality – up to 1920 x 1440 resolution and 200Mhz bandwidth

- No software required – easy PC selection via Push Buttons and Hot-Key Operation

- Hot-Plug feature – add or remove PC’s without powering off the KVM switch or other PC’s

- Auto-Scan Mode for monitoring PCs, with configurable scan interval from 5~99 seconds

- Keyboard status restored when switching PCs

- LED Display for easy status monitoring

- Beeping sound for port switching confirmation

- EIA-19” rack-mountable (hardware included)

- 1-Year Warranty

TREND SPEC’S

Computer Port:	8 ports. Keyboard and Mouse: PS/2 type mini Din 6-pin (female),

VGA: HDDB 15-pin (female)

Console Port:		1 port. Keyboard and Mouse: PS/2 type mini Din 6-pin (female),

VGA HDDB 15-pin (female)

PC Selection:		Hot-Keys and Push Buttons

LED Segment:		Two LED indicators per port (PC Link (green) and PC Active (red))

Auto-Scan Intervals:	5~99 seconds

Keyboard State:	Saved and restored

Video Bandwidth:	200MHz

Power Adapter:	External Power adapter, 12VDC, 1A (or 9VDC, 1A)

Dimensions:		410 x 165 x 45 mm (16.14 x 6.5 x 1.77 inches)

Weight:		Approximately 2.2 Kg. (4.85 lbs)

Operating Temp.:	0(~40( C (32(~104( F)

Storage Temp.:	-20(~60( C (-4(~140( F)

Operating Humidity:	0~80%, Non-Condensing

Certifications:		FCC, CE

TOP REASONS THE TK-801R IS A LASTING TREND

Integration Friendly:	Does not require driver/software for the installation and operation. Switching between PC’s with the Push Buttons and Hot-Key operation.

Flexible:	Hot-Plug feature – add PC’s or remove connected PC’s without powering off the KVM Switch or the other PC’s.

Cost Effective:	Manage multiple PC’s with single keyboard, monitor, and mouse. Save on equipment cost, utility, and space.

Performance:	Support very High Video Quality up to 1920 x 1440 with 200Mhz bandwidth. Keyboard status is saved for each PC.

TK-801R		8-Port Rack Mount KVM Switch

TK-200K		2-Port KVM Switch Kit

TK-400K		4-Port KVM Switch Kit

TK-401R		4-Port Rack Mount KVM Switch

TK-205i		2-Port KVM Switch with Integrated Cables

TK-802R		8-Port Stackable Rack Mount KVM Switch (with OSD)

TK-C06		6-Feet KVM Cable (male-to-male)

TK-C10		10-Feet KVM Cable (male-to-male)

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

Sales: sales@trendware.com • Support: techsupport@trendware.com	ss03052003-2

# Text boxes

8-Port Rack Mount KVM Switch

TRENDnet’s TK-801R 8-Port KVM Switch allows you to manage 8 PC’s with just one keyboard, monitor, and mouse.  Switch between PC’s with a simple press of a button!  Eliminate the hassle of cable swapping and save money and space with TRENDnet’s TK-801R. With its rack-mount size and slim one unit height, it is perfect for mounting on EIA-19” rack in the Equipment Room and Computer Lab.  Rich in features such as, Hot-Plug, Auto-Scan, and Hot-Key Operation, TRENDnet’s TK-800R is the perfect choice for managing multiple PC’s.

TK-801R

KVM Applications

For TK-801R

Product Information