Features

- Up to 14Mbps High-Speed Data Transfer Rate over Powerlines

- Allows Concurrent Shared Internet Access across existing Electrical Outlets

- Supports up to 12 Clients per Network

- Fully HomePlug 1.0.1 Compliant

- Supports 56-bit Data Encryption Security

- Compatible with Windows 98(SE), ME, 2000 and XP

- Connect to a Network using Existing Powerlines with Wall-Plugged design

- Range of up to 300 Meters (depends on the environment)

- Supports Plug & Play and Easy Installation

- 3-Year Warranty

Specifications					   Powerline Networking Solution

| Hardware |
| --- |
| Standards | IEEE 802.3, IEEE 802.3U HomePlug 1.0.1 |
| Interface | 10/100Mbps Auto-MDIX RJ45 Port Power Prongs |
| Frequency Band | 4.3 ~ 20.9 MHz |
| Access Method | CSMA/CA |
| Modulation | OFDM |
| Speed | Powerline: Up to 14Mbps RJ45: 10/100Mbps |
| OS Compliant | Windows 98SE/ME/2000/XP |
| Nodes | Up to 12 client notes |
| Encryption | 56-bit DES with key management |
| LED | Power, Link, Activity, Collision |
| Dimension (L x W X H) | 68 x 43 x 95 mm (2.7 x 1.7 x 3.7 inches) |
| Weight | 113g (4 oz.) |
| Power Source | 100~240VAC, 50/60 Hz |
| Temperature | 0° ~ 70° C (32° ~ 158° F) |
| Operating Humidity | 0% to 90% (Non-Condensing) |
| Certifications | FCC, CE, HomePlug 1.0.1 |

Package Contents			Related Products

- TPL-102E				- TPL-101U

- Quick Installation Guide		- TPL-110AP

- Utility CD-ROM			- TPL-111BR

To order please call: 888-326-6061 • Sales: sales@trendware.com

Support: techsupport@trendware.com • Tech Support Hotline: 1(310) 626-6252

Official Site: www.TRENDnet.com

# Text boxes

Powerline 10/100Mbps Ethernet Bridge

The Powerline 10/100 Mbps Ethernet Bridge transforms existing power lines in your home or small office into a high-speed network solution.  The Powerline Ethernet bridge meets Home Plug 1.0.1 compatibility, ensures privacy through 56-bit Data Encryption, and supports data rates of up to 14Mbps. Included software measures data performance and enhances network security.

TPL-102E