Features

- Wi-Fi Compliant with 802.11b/g Standards

- Up to 125Mbps High Speed over Wireless Connection (Afterburner Technology) (in Access Point Mode only)

- Up to 14Mbps High-Speed Data Transfer Rate over Powerlines

- Built-in 4 x 10/100Mbps Auto-MDIX LAN Ports

- Built-in 1 x 10/100Mbps Auto-MDIX WAN Port (Internet)

- Supports Cable/DSL Modems with Dynamic IP, Static IP, PPPoE, or PPTP Connection Types

- Supports Access Point and Wireless Distribution System (WDS) Bridge/Repeater Modes

- Dynamic Data Rate Scaling at 54, 48, 36, 24, 18, 12, 9 and 6Mbps for 802.11g

- Dynamic Data Rate Scaling at 11, 5.5, 2 and 1Mbps for 802.11b

- Supports ESSID Enable/Disable Feature, AP Isolation and  LAN MAC Address Filtering

- Supports 64/128-bit Wired Equivalent Privacy (WEP) , WPA and WPA-PSK

- Supports Static and Dynamic Routing

- Compliant with Windows 95/98/NT/2000/XP/2003 Server, Linux and Mac OS

- Powerline Range of up to 300 meters (depends on the environment) and up to 12 clients support

- Wireless Range of 30 ~ 100 meters Indoor (depends on the environment)

- Wireless Range of 50 ~ 300 meters Outdoor (depends on the environment)

- Connect to a Network using exiting Power Lines with Wall-Plugged Design

- 3-Year Warranty

Specifications

| Hardware |  |
| --- | --- |
| Standards | Wireless: IEEE 802.11b (11Mbps), IEEE 802.11g (54Mbps) Wired: IEEE 802.3, IEEE 802.3u IEEE 802.1x, HomePlug Powerline Alliance Industry Specifications V1.0 |
| LED Indicators | Power, WLAN_TX/RX, LAN, WAN, HOMEPLUG(Activity/Collision) |
| Network Protocols | TCP/IP, IPX, UDP, DHCP Client, DHCP Server |
| Power Source | Input: AC 120V, 0.1A, 50/60Hz |
| Dimensions (LxWxH) | 198 x 160 x 33 mm (7.8 x 6.3 x 1.2inches) |
| Weight | 0.7kg (1.54 lbs) |
| Temperature | Operating: 0(~ 40(C (32(F~ 104(F) Storage: -20(~ 65(C (-4(F~ 149(F) |
| Humidity | Operating: 10% ~ 85% Storage: 5% ~ 90% |
| Certification | FCC, CE |
| Powerline |  |
| Data Rate | Up to 14Mbps Transfer Rate |
| Nodes | Support up to 12 clients per Network |
| Security | 56-bit DES Encryption |
| Wireless |  |
| Module Technique | 802.11b: DSSS 802.11g: OFDM |
| Frequency Range | 2.4 ~ 2.4835 GHz |
| Antenna | 1 x Attached 2dBi Antenna |
| Data Rate (auto fallback) | 802.11b: 11Mbps, 5.5Mbps, 2Mbps, and 1Mbps 802.11g: 54Mbps, 48Mbps, 36Mbps, 24Mbps, 18Mbps, 12Mbps, 9Mbps and 6Mbps High Speed-G: 125Mbps (Afterburner technology, Enhanced Throughput by up to 40%) |
| Security | 64/128-bit WEP WPA and WPA-PSK (TKIP, AES, TIP+AES) 802.1x (Port-based Security with RADIUS) |
| Transmit Power | 13.5 ±1.5dBm (typical) |
| Receiving Sensitivity (802.11a/b/g) | 11Mbps 10 – 5 BER @ -80 dBm 54Mbps 10 – 5 BER @ -65 dBm |
| Channels | Universal Domain Support (Channel 1~14) |

Package Contents			Related Products

- TPL-111BR				- TPL-101U

- Quick Installation Guide		- TPL-102E

- Utility CD-ROM			- TPL-110AP

- Cat.5 Cable (1.5m/5ft)

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

### Sales: sales@trendware.com • Support: techsupport@trendware.com

Tech Support Hot Line: 1-310-626-6252

### Official Site: www.TRENDNET.com

# Text boxes

TPL-111BR

125Mbps 802.11g Wireless Powerline Router

The Wireless Powerline Router removes additional costs in network cabling by using existing power lines in your home or small office to network several wireless workstations.  Secure file sharing, an Internet connection, or other network resources by using 56-bit DES for 14Mbps power line transmission and WPA security for 125Mbps wireless transmission.

Powerline Networking Solution