Features

- Up to 85Mbps High-Speed Data Transfer Rate over Powerlines

- Allows Concurrent Shared Internet Access across existing Electrical Outlets

- Fully HomePlug 1.0 Turbo Compliant

- Supports 56-bit Data Encryption Security

- Compatible with Windows 98SE, ME, 2000 and XP Operating Systems

- Connect to a Network using Existing Powerlines with Wall-Plugged design

- Supports up to 16 Clients per Network with range of up to 300 meters

- Supports Plug & Play and Easy Installation

- 3-Year Warranty

Specifications					   Powerline Networking Solution

| Hardware |
| --- |
| Standards | IEEE 802.3, IEEE 802.3u HomePlug 1.0 Turbo |
| Interface | 10/100Mbps Auto-MDIX RJ45 Port Power Prongs |
| Frequency Band | 4.5 ~ 21 MHz |
| Modulation | OFDM |
| Speed | Powerline: Up to 85Mbps RJ45: 10/100Mbps |
| Supported OS | Windows 98SE/ME/2000/XP |
| Nodes | Up to 16 client notes |
| Encryption | 56-bit DES with key management |
| LED | Power, HomePlug, Ethernet |
| Dimension (L x W X H) | 74 x 100 x 35 mm (2.9 x 4 x 1.3 inches) |
| Weight | 140g (5 oz.) |
| Power Source | Input: 100~240V AC, 50/60 Hz |
| Consumption | 2.5 watts (max.) |
| Temperature | 0° ~ 40° C (32° ~ 104° F) |
| Operating Humidity | 0% to 90% (Non-Condensing) |
| Certification | FCC, CE |

Package Contents				Related Products

- TPL-202E					- TPL-210AP

- Multi-Language Quick Installation Guide

- Utility CD-ROM

- RJ-45 Cable (1.8m)

To order please call: 888-326-6061 • Sales: sales@trendnet.com

Support: techsupport@trendnet.com • Tech Support Hotline: 1866-845-3673

Official Site: www.TRENDnet.com

# Text boxes

85Mbps Powerline Fast Ethernet Bridge

The Powerline 10/100 Mbps Ethernet Bridge transforms existing power lines in your home or small office into a high-speed network solution.  The Powerline Ethernet bridge meets Home Plug 1.0 compatibility, ensures privacy through 56-bit Data Encryption, and supports data rates of up to 85Mbps. Included software measures data performance and enhances network security.

TPL-202E (v1.0R)