Features

- Built-in one 10/100Mbps Auto-MDIX Fast Ethernet LAN port

- Embedded one 3.5” IDE Hard Drive bay (HD not included)

- Built-in two USB 2.0 portsfor additional storage devices

- Support two modes: Open mode and Account Mode

- Provides FTP Server for remote access

- High security support with IP address filtering to ALLOW or DENY access

- Support USB storage devices such as hard-disk, flash disk and CD-ROM

- Schedule downloads with FTP or HTTP without turning on the PC

- Provides email notification service when HD is full, critical error or  modification information

- Support real time clock (RTC) and UPnP for Windows XP

- Compliant with Windows 98(SE)/ME/NT/2000/XP and Linux SMB Operation System

- Provides Easy-Search utility for different IP domain setting

- 2-Year Warranty

Specifications

| Hardware |
| --- |
| Standards | IEEE 802.3 / IEEE 802.3u USB 2.0, 1.1 |
| Microprocessor | RDC 3210 (150Mhz) |
| Flash ROM / RAM | 4MB Flash / 32MB SDRAM |
| IDE Controller | ITE IT8211F |
| Interface | Power / Reset / Un-mount USB buttons 1 x 10/100Mbps Auto-MDIX RJ-45Port 2 x USB 2.0 Type A port (Hard-Disk/Flash-Disk/CD-ROM, not included) 1 x Internal IDE HD Bay (HD not included) |
| LED | Power, LAN, IDE HDD, IDE HDD Full |
| Power Consumption | 36 watts (max) |
| Power | 12V DC, 3A |
| Dimensions | 200 x 154 x 60mm (7.9 x 6 x 2.4in) |
| Weight | 0.7kg (1.5 lb) |
| Temperature | Operation: 5(C ~ 40(C (41(F ~ 104(F) Storage: -20(C ~ 50(C (-4(F ~ 122(F) |
| Humidity | 90% ~ 95% (Non-Condensing) |
| Emissions | CE, FCC |
| Software |
| Real Time OS | Embedded Linux (Kernel version 2.4.25) |
| Network Transfer Protocol | TCP/IP |
| Network File Protocols | Microsoft Networks (CIFS / SMB) Internet (HTTP 1.1) FTP |
| Supported HD Type | ATA/IDE up to ATA/133 |
| File System Type | IDE Drive: EXT2 USB Drive: FAT16 / FAT32 / EXT3 / EXT2 / NTFS (read only) |
| Disk Management | Hard Disk Failure Detection (S.M.A.R.T) Disk Used Status Management |
| System Management | Web Management (Internet Explorer 5.0 or later) System Temperature Monitor System Software Upgrade Support Network Time Protocol Multi0Users Account / Session Setting |
| System Monitoring | System Log E-Mail Alert IP Address Filtering (Allow or Deny) Account permissions for directory |

Package Contents							Related Product

- TS-I300								- TS-I300W

- Multi-Language Quick Installation Guide	- TU2-400

- CD-ROM (User’s Guide & Utility)

- RJ-45Cable

- Power Adapter (12V DC, 3 A)

To order please call: 888-326-6061 • Sales: sales@trendnet.com

Support: techsupport@trendnet.com • Tech Support Hotline: 1(866)845-3673

Official Site: www.TRENDnet.com

# Text boxes

USB 2.0 & IDE Network Storage

Enclosure

The USB 2.0 IDE Network Storage Server is perfect for adding storage to your network.  It includes a Web based utility for simple configuration and management. Most major operating systems are supported. The USB 2.0 IDE Network Storage Server is a simple and secure solution for expanding network storage.

TS-I300 (v1.0R)