Features

- Compliant with USB 1.1 Specifications

- Compliant with IEEE 1284 (Bi-Directional Parallel) Interface

- Supports Suspend/Normal Power Management Modes

- Supports Data Transfer Rate up to 12Mbps Speed

- Compliant with Windows 98(SE)/ME/2000/XP

- Eliminate Manual or Automatic Parallel Switch Boxes

- Supports Plug & Play and Easy Installation

- 2-Year Warranty

Specifications					Solution for TU-P1284

| Hardware |
| --- |
| Interface | USB 1.1 Interface Type A IEEE 1284 Centronics 36 Male |
| OS Compliant | Windows 98(SE)/ME/2000/XP |
| Cable Length | 2m/6.7ft. |
| Cable Gauge | 28/24 AWG |
| Data Rate | 12Mbps |
| Power Consumption | 500mA (max) |
| Weight | 126g. (0.3 lb) |
| Operating Temperature | 0( ~ 40( C (32( ~ 104( F) |
| Storage Temperature | -10( ~ 45( C (14( ~ 113( F) |
| Humidity | 85% (Non-Condensing) |
| Certification | FCC, CE |

Package Contents		System Requirement

- TU-P1284			- Intel Compatible 486DX-66MHz CPU or Higher

- Quick Installation Guide	- 1 x USB 1.1 Compliant Port

- Driver CD-Rom		- Windows 98(SE)/ME/2000/XP Operating System

# Text boxes

TU-P1284

USB to Parallel 1284 Converter

This USB to Parallel 1284 converter allows you to connect a parallel printer to a USB port on your desktop or laptop pc.