Features

- 4 x External Type A USB 2.0 Ports

- 1 x Internal Type A USB 2.0 Port

- 32-bit 33Mhz Host Interface Compliant to PCI Specification 2.2

- Supports PCI-Bus Power Management Interface Specification 1.1

- Compliant with USB 2.0 and USB 1.1 Specifications

- OHCI 1.1 (Open Host Controller Interface) Compliant

- EHCI .95 (Enhanced Host Controller Interface) Compliant

- Supports all USB speeds: Low-Speed (1.5Mbps), Full-Speed (12Mbps) and High-Speed (480Mbps)

- Switches to the Peripheral’s Highest Supported Speed Automatically

- Fully Forward and Backward Compatible with USB 1.1 Devices

- Supports up to 127 USB Devices

- Compatible with Windows 98SE/ME/2000/XP/2003 Server and Mac OS 10 or above

- Supports Plug & Play and Easy Installation

- 2-Year Warranty

Specifications				                   Solution for TU2-H5PI

| Hardware |
| --- |
| Interface | 32-bit PCI rev. 2.2 |
| Controller | OHCI, EHCI |
| Standards | USB 2.0 & USB 1.1 |
| Ports | 4 x External USB 2.0 Ports 1 x Internal USB 2.0 Port |
| OS Compliant | Windows 98SE/ME/2000/XP/2003 Server Mac OS 10.x or above |
| Data Rate | High-Speed: 480Mbps Full-Speed: 12Mbps Low-Speed: 1.5Mbps |
| Power Consumption | 500mA (max) per port |
| Dimensions (LxWxD) | 134 x 121 x 21.6mm (5.2 x 4.76 x 0.85 inches) |
| Weight | 70g. (0.15 lb) |
| Operating Temperature | 0( ~ 40( C (32( ~ 104( F) |
| Storage Temperature | -10( ~ 45( C (14( ~ 113( F) |
| Humidity | 0 ~ 85% (Non-Condensing) |
| Certification | FCC, CE |

Package Contents			System Requirement

- TU2-H5PI				-    PC with Supported Operating Systems

- Quick Installation Guide			-    Available PCI Version 2.2 Slot

- CD-ROM (Driver & User’s Guide)		-    CD-ROM Drive for Driver Installation

# Text boxes

TU2-H5PI

5-Port USB 2.0 Host PCI Adapter

This 5-Port USB 2.0 Host PCI Adapter gives your Desktop PC five USB 2.0 ports so you can easily connect your peripherals and enjoy the benefits of high-speed USB 2.0!

TU2-H5PI (v1.1R)