Features

- Wi-Fi Compliant with IEEE 2.4GHz 802.11b/g Devices

- Wireless Supports Infrastructure and Ad-Hoc Modes

- Supports 128-bit WEP and WPA-PSK Encryption

- Supports CCD image sensor and DC-Iris control

- Supports audio monitoring and RS-485 port for pan & tilt Control

- Includes I/O ports to trigger alarm and e-mail notification

- Built-in Microphone for audio monitoring

- High quality Motion JPEG and MPEG-4 Video Recording for up to 30 frames per second.

- Equipped with IR Lens (10 meters) for day & night vision

- Supports viewing and recording up to 16 cameras at the same time*

- Progressive scan, all lines are captured at the same time

- Supports 4x digital zoom

- Supports video overlay in both graphics and texts.

- Supports three adjustable motion detection windows with just in time snapshot

- Supports TCP/IP networking, SMTP e-mail, HTTP and other Internet related protocols

- Supports Web configuration with password protection

- Supports UPnP and DDNS

- Multiple cameras monitoring, image capturing, and video recording (Windows 98/ME/2000/XP)

- Broad range of applications for monitoring homes, offices, banks, hospitals, parking lot and a variety of private and public monitoring

- 3-Year Warranty

* Monitoring multiple cameras may require a high performance CPU

Specifications

| Camera Specifications | Hardware Specifications |
| --- | --- |
| Image Sensor | System |
| Sensor | Sony 1/4” progressive CCD | CPU | Infineon ADMTek 5120 |
| Resolution | 640 x 480, 320 x 240, 160 x 120 | RAM | 32Mbyte |
|  |  | ROM/Flash | 4Mbytes |
| Lens Type (Replaceable) | f: 6.0mm F: 1.8 CS Mount IR Lens | OS | Linux |
|  |  | I/O & Control |
| Minimum Illumination * | 0.5 Lux at F1.8 1/30 sec Exposure Time (Max 30 fps) 0.1 Lux at F1.8, 1/5 sec Exposure Time (Max 5 fps) 0 Lux at F1.8 IR LED Enabled Mode | Generic Input | 1 Set (Pin 1, 2) |
|  |  | Generic Output | 2 Sets (Pin 3,4 & Pin 5, 6) |
|  |  | RS-485 (For pan/tilt Control) | 1 Set (Pin 7, 8) |
|  |  | System Requirement (Web Configuration) |
|  |  | CPU | Intel Pentium 1GHz or Above |
|  |  | Memory Size | 256MB |
|  |  | Resolution | 800 x 600 or above |
|  |  | Physical/Environment |
|  |  | Dimension | 157 x 62 x 56mm (6.2 x 2.4 x 2.2in.) |
| Audio Input & Output |  |  |
| Input | Built-in Mic External Mic (mono) | Weight | Camera: 450g (15.9oz) Stand: 116g (4.1oz.) |
| Compression | ADPCM (mono) PCM: 8K/16K/24K/48K (mono) | Power | 12V DC, 1.5A External Power Adapter |
| Signal to Noise Ratio | 62dB | Consumption | 7 Watt |
|  |  | Temperature Operation Storage | 5ºC ~ 45ºC (41ºF ~ 113ºF) -10ºC ~ 60ºC (14ºF ~ 140ºF) |
| Video Compression |  |  |
| Compression | MPEG-4( Simple Profile) M-JPEG |  |  |
|  |  | LED | Power: green, Link: green |
| Resolution | VGA/QVGA | Humidity | 15 % ~ 85% Non-Condensing |
| Frame Rate | 30fps@VGA, QVGA | Certification | CE/FCC |
| Up/Down Reversal | Yes | Wireless |
| Left/Right Reversal | Yes | Standard | IEEE 802.11b/g |
| Quality Selection | 5 Levels | Data Rate | 11g: 54, 48, 36, 24, 12, 9 & 6Mbps 11b: 11, 5.5, 2 & 1Mbps |
| Frame Rate Selection | 13 Levels |  |  |
| Brightness/Contrast/Color/Sharpness/ Motion Detection | Yes |  |  |
|  |  | Frequency | 2.4 ~ 2.4835Ghz (ISMB) |
|  |  | Antenna | Detachable 2dBi Diversity Antenna (Reverse SMA)Connector) |
| Anti-Flicker | 50Hz or 60Hz |  |  |
| Expose/White Balanced Control | Automatic |  |  |
|  |  | Security | 64/128-bit WEP |
| Communication | Software |
| LAN | 10/100Mbps Ethernet Auto-Sensed & Auto MDIX | Browser | Internet Explorer 5.0 or above |
| Protocol | HTTP, SMTP, FTP, Telnet, NTP, DNS, DHCP, TCP/IP DDNS, UPnP | Application | IPView Pro Software |
|  |  | OS Support | Windows 98SE/ME/2000/XP |

* The Camera has an "ambient light sensor" on the IR assembly.  This Sensor detects the ambient light and turns on the IR LEDs when the ambient light gets below 10 Lux.

Package Contents							Related Product

- TV-IP301W								- TV-IP201

- Multi-Language Quick Installation Guide				- TV-IP201W

- Utility CD-ROM							- TV-IP301W

- Camera Stand							- TV-IP400

- RJ-45 Cable								- TV-IP400W

- Power Adapter 12V, 1.5A

To order please call: 888-326-6061 • Sales: sales@trendnet.com

Support: support@trendnet.com  • Tech Support Hotline: 866-845-3673

www.trendnet.com

# Text boxes

Advanced Day/Night 
Wireless Internet Camera Server with Audio

The Advanced Day/Night Wireless Internet Camera Server with Audio is perfect for transmitting real-time video over the Internet. This camera provides high quality streaming video with frame rates up to 30fps. This 802.11b/g camera transmits secured video wirelessly. Users can view up to 16 cameras on one screen at any time.

Network Solution for TV-IP301W

TV- IP301W version V1.0R