Features

- Supports Router (Router+Modem) or Modem (Modem only) Mode

- Compliant with ADSL, ADSL2, ADSL2+ on G.dmt, G.lite and T1.413 Multi-Mode PSTN Environments

- Compliant with PPPoE, PPPoA or IPoA Connection Types

- Supports Filtering by URL, MAC Address, Services and Date/Time

- Supports Virtual DMZ, Virtual Servers (Port Forwarding) and Firewall Rules

- Supports RIP/Static Routing and Dynamic DNS Service

- Supports up to 100 VPN Pass-Through sessions for PPTP, IPSec or L2TP connections

- NAT/NAPT, Rule-Based and SPI Firewall protect against DoS (Denial of Service) attacks

- Real-Time email alert and logs when attack/unauthorized Internet activity occurs

- DHCP Server feature supports up to 253 Users

- Supports UPnP (Universal Plug & Play) and ALGs Support Internet applications such as Email, FTP, Gaming, MSN

Messenger, Yahoo Messenger, PING, Telnet, and more

- Supports most operating systems, such as Windows 95/98/ME/NT/2000/XP, Unix, and Mac

- Easy Configuration and Remote Management with Web Browser (HTTP)

- Built-in Flash memory for firmware upgrade

- 5-Year Warranty

Specifications

| Hardware |
| --- |
| Standards | IEEE 802.3 10Base-T; IEEE 802.3u 100Base-TX |
| Protocols | DHCP Client Server (LAN) SMTP NTP (Network Time Protocol) DHCP Client (WAN) |
| Firewall | NAT Attack Alert (Email) and Log Denial of Service (SPI) Access Control Fort Forwarding Port Range Forwarding Schedule-Based URL Content Filtering |
| Security | URL Filter, Access Control, Local Password |
| VPN Pass Through | PPTP, IPSec, L2TP (up to 100 sessions) |
| VPN IPSec Client | Up to 8 Simultaneous IPSec Tunnels Throughput 1.5Mbps DES/3DES |
| ATM | TM Cell over AAL5 Support UBR/CBR/VBR VPI Range (0-255) and VCI range (32-65535) Support 4PVCs Support OAM F4/F5 loop back Payload Encapsulation RFC2684 (RFC 1483 / 2684), multi-protocol over ATM RFC2684 (RFC 1483 / 2684), Bridge mode RFC2225 (RFC 1577), IPoA RFC2364, PPP over ATM (CHAP and PAP supported) RFC2516, PPPoE (PPP over Ethernet) over ATM Support auto-detection for VPI/CVI (VPI: 0~10, VCI: 32~90) and multiplexing method (VC-based, LLC-based) |
| Routing | Cross Segment Static Route RIP1, RIP2 |
| Management | Web-Based Management (HTTP) Remote Management via WAN port |
| WAN Port (ADSL line Interface) | Complies with G.dmt (G.992.1) Annex A Complies with G.lite (G.992.2) and T1.413 Annex A ITU G.992.3 Annex A ADSL2, ITU G.992.5 Annex A ADSL2+ RJ-11 connector, Line Impedance: 100 Ω |
| LAN Port | 4 x 10/100Mbps Auto-MDIX and Auto-Negotiation RJ-45 Port |
| Flash | 4Mbytes |
| DRAM | 16Mbytes |
| Reset Button | Reset to Factory Default |
| LED | Power, Status, 4x100LAN, 4x10LAN, ADSL, Internet |
| Power | 12V DC 1A External Power Adapter |
| Dimensions | 175 x 115 x 30mm (6.9 x 4.5 x 1.2 inches) |
| Weight | 280g (9.9 oz) |
| Temperature | Operating: 0˚~ 40˚C (32˚~ 104˚F) Storage: -20˚~ 70˚C (-4˚~ 158˚F) |
| Humidity | Operating: 10 ~ 90% RH Storage: 5 ~ 95% RH |
| Emissions | FCC, CE |

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

Tech Support Hotline: (866)845-3673

Sales: sales@trendnet.com • Support: support@trendnet.com

www.TRENDNET.com

# Text boxes

New Implements

- New Standing Style Housing

- RoHS Compliant Hardware

Package Contents

- TW100-BRM504

- Quick Installation Guide

- CD-ROM (User’s Guide)

- 1 x 1.5m (5ft.) Cat.5 Cable

- 1 x RJ11 Telephone Cable

- Power Adapter (12V DC 1A)

Related Products

- TW100-BRV204

- TW100-BRV304

- TEW-435BRM

4-Port ADSL Firewall Modem Router

TW100-BRM504 includes an ADSL/ADSL2/ADSL2+ Modem, SPI Firewall, Router, and 4-Port Switch ALL-IN-ONE box. Simply plug it into your DSL phone line and you have a high-performance network for your home or small office. Security includes a Stateful Packet Inspection Firewall (SPI), Denial of Service Attack prevention, VPN pass-through, and advanced Rule-Based Firewall, while the Application Level Gateway (ALG) and Port Forwarding features add flexibility so designated programs such as gaming and web-conferencing programs can work around the Firewall. Set-up is easy with UPnP support and a Quick Install Wizard.

TW100-BRM504 (C1.0R)