TK-802R

8-port Stackable Rack-Mount KVM Switch w/ OSD

Quick Installation Guide

Thank you for purchasing the TK-802R Stackable Rack Mount KVM Switch. With our highly reliable and quality product, user can enjoy countless benefits from using it.

TK-802R KVM Switch

Before you install

The default setting of the TK-802R Stackable Rack-Mount KVM Switch is appropriate for most systems.  In fact, you do not have to make any configuration before installation. It’s a out-of-the-box installation: Just connect and set up the cable connections for the KVM Switch(es) and your computers, power up the Switch(es) and boot up the computers and you can start to operate immediately.

For a quick start on installation and operation, please follow the instructions below.

The correct boot up sequence is ……

- Power up your KVM Switch(es) first. If you want to set up multiple daisy-chained KVM Switches, you have to power them all up and then perform the initialization (that is, perform a reset on the master KVM Switch. Also remember to have the shared Keyboard, monitor and mouse connected to your master KVM Switch before you power it up.

(2) After you have powered up your KVM Switch(es), power up your connected computers (in any order).

Out-of-the-box Installation

Take the KVM Switch out of the box and begin installation.

Before connecting any cable to your KVM Switch, please make sure all of your computers and their peripherals have been powered off.

Step 1. Make sure all the computers that are to be connected to the KVM Switch and their peripherals are powered off.  If not, power them off before you proceed with the following steps.

Step 2. Connect the shared keyboard, monitor and mouse to the Console Connectors on the rear of the Master KVM Switch and then connect the AC Power Adapter to the power outlet and the KVM Switch.

Although the KVM Switch receives power through the PC’s PS/2 interface, it is necessary to install the external power adapter to provide sufficient power for both the OSD operation and the daisy-chain (stacking) application.  If the external power is not attached, the KVM Switch may become unstable.

If you use only a single KVM Switch, please skip step 3, 4 and 5. Go directly from step 2 to step 6.

If you would like to daisy-chain multiple KVM Switches, please go to step 3.  You could daisy-chain up to 16 levels of KVM Switches with a maximum of 128 PCs connected.

Step 3. Use a daisy-chain cable (one that similar to the 3-in-1 combo cable) to connect the daisy-chain port of the master KVM Switch to the console port of the second KVM Switch. Connect the power adapter cord to the second Switch to power it on.

Step 4. If you have yet another Switch to be daisy-chained, just repeat

Step 3 and connect them together. You can daisy-chain up to 16 units of KVM Switches.

Step 5. Initialize the daisy-chained Switches by performing a reset on the master KVM Switch. Press and hold down Button 1 for at least 3 seconds to reset the whole daisy-chained Switches.

DO NOT PRESS Button 1 on any slave Switch, doing this will initialize only the Switches “downstream” from this slave Switch.

You can also use the hotkey sequence: ScrLk, ScrLk , End  for daisy-chain initialization.

Step 6. Now the KVM Switch or daisy-chained KVM Switches should have been powered-up and initialized….) Connect each of your computer to a PC port on the rear of the Switch(es). You can use individual standard keyboard, mouse and video cables for connection, although the 3-in-1 combo cable is highly recommended for your convenience.

Step 7. Power up the connected computers. After your computers are powered up, the keyboard and mouse will be recognized and now you can begin operating the Switch.

DO NOT TRY to power up the computers first before you power up the KVM Switch.  Otherwise, the computers will have difficulty recognizing your shared keyboard and mouse.

Easy Operation

There are three methods to select a specific computer on a specific Switch, using the front-panel push button, hotkey sequence or OSD Menu option.

Front-panel push buttons

The front-panel buttons let you have direct control over KVM Switch operation and channel switching. Simply press the channel button on the Switch to select switch to that channel (PC). See Quick Reference Sheet

Keyboard hotkeys

Keyboard hotkey sequence consists of a combination of at least three specific keystrokes:  See Quick Reference Sheet

Hotkey sequence = ScrLk , ScrLk , Command key(s)

The two consecutive ScrLk keystrokes should be pressed within 2 seconds and the following command key(s) should also be pressed within 2 seconds after the last ScrlK keystroke. Otherwise, the hotkey sequence will not be validated.

For detailed Hotkey sequences and their corresponding functional commands, please see  Quick Reference Sheet.

.

OSD Menu

To activate the OSD (On Screen Display) Menu, use the hotkey sequence:

Activate OSD  =  ScrLk , ScrLk , Space Bar

| QUICK REFERNCE SHEET for KVM Switch Operation Commands Hotkeys/ OSD Menu / Front-Panel Buttons |
| --- |
| Command | Hotkeys | OSD control1 | Front-panel | Description | User Guide |
| Select PC | ScrLk , ScrLk , x (bank no.) , y (channel no.) | Arrow keys ((() to highlight channel number, Enter to select | Press corresponding button yz on Switch x for channel yz on bank x. | Select the active bank (Switch) and channel (computer) | Page 22 |
| Next lower channel | ScrLk , ScrLk , ↑ (arrow up) | Arrow keys ((() to highlight channel number, Enter to select | Press the desired channel button | Select the next lower connected channel | Page 23 |
| Next higher channel | ScrLk , ScrLk , ↓ (arrow down) | Arrow keys ((() to highlight channel number, Enter to select | Press the desired channel button | Select the next higher connected channel | Page 23 |
| Next lower bank | ScrLk , ScrLk , PgUp | PgUp | Press the desired channel button | Select the next lower bank (Switch) when multiple Switch units are daisy-chained together | Page 23 |
| Next higher bank | ScrLk , ScrLk , PgDn | PgDn | Press the desired channel button | Select the next higher bank (Switch ) when multiple Switch units are daisy-chained together | Page 24 |
| Autoscan Beep Sound On/Off | ScrLk , ScrLk , B | -- | -- | Toggle on/off the beep sound for switching confirmation during auto-scanning operation | Page 24 |
| Reflash EEPROM | ScrLk , ScrLk , R | -- | -- | Restore all settings to factory default (except the password) | Page 24 |
| Find PC by Name | ScrLk , ScrLk , F | -- | -- | Search the presence of a specific PC by its name | Page 25 |
| Change PC Name | -- | Arrow keys ((() to navigate, Ins key to edit PC name | -- | Change the PC name | Page 26 |
| Reset / Initialize KVM | ScrLk , ScrLk , End | -- | Button 1 (Press and hold it down for 3 seconds) | Reset/reboot/initialize daisy-chain (also activates password protection) | Page 26 |
| Show OSD Menu | ScrLk , ScrLk , Space Bar | -- | -- | Activate the OSD Menu | Page 26 |
| Autoscan | ScrLk , ScrLk , S | -- | Last button (Channel 8; press and hold it down for 3 seconds) | Autoscan every connected channel for quick browsing on each channel. | Page 26 |
| Stop Autoscan | Esc | -- | Press any push button | Terminate Autoscan mode | Page 26 |
| Autoscan Delay | -- | Arrow keys ((() to navigate, Enter to select and edit | -- | Specify delay time within a range of 5 ~ 99 seconds (default = 10 sec.) | Page 27 |
| OSD Remain Time | -- | Arrow keys ((() to navigate, Enter to select and edit | -- | Change the OSD Menu Remain Time | Page 27 |
| Password Config | -- | Arrow keys ((() to navigate, Enter to select and edit | -- | Enable/disable password protection | Page 27 |
| Password Change | -- | Arrow keys ((() to navigate, Enter to select and edit | -- | Change the password | Page 28 |

Quick   Reference   Sheet