## FEATURES

- Built-in 4-port 10/100Mbps Auto-Sensing Switch

- Supports most operating systems, such as Windows 95/98/ME/NT/2000/XP, Unix, and Mac

- Compliant with ITU-T G.dmt, G.lite and multi-mode for ADSL modems

- Support PPPoE, PPPoA and IPoA

- Website Access Control using URL Keywords and Services Types

- NAT/NAPT Firewall and Stateful Packet Inspection (SPI) to protect against DoS attacks

- Supports DMZ, Virtual Servers (Port Forwarding) and Firewall Rules

- Supports RIP/Static Routing and Dynamic DNS Service

- Supports 100 sessions of VPN Pass-Through for PPTP, IPSec and L2TP

- Real-Time e-mail alert and logs when attack/unauthorized Internet activity occurs

- DHCP Server supports up to 253 clients

- Supports UPnP (Universal Plug & Play) and ALGs Supports Internet applications such as Email, FTP,

Gaming, ICQ, NetMeeting, PING, Telnet, and more

- Remote Management with HTTP/Web Browser (from LAN, WAN, or both)

- Easy Configuration using Web Browser

- Flash memory for firmware upgrade and save/restore router configuration

- 5-Year Warranty

## TREND SPEC’S

Standards:	IEEE 802.3(10Base-T), 802.3u(100Base-TX)

Protocols:	NAT/NAPT, PPPoE & PPPoA, HTTP, DHCP(client/server), TCP/IP &UDP, PAP&CHAP, RIP1, DDNS, UPnP

Firewall:	NAT firewall, Rule-Based Policy Firewall, Attack Alert (email) and log, Stateful Packet Inspection firewall for DoS (Denial of Service) Attacks

Security:	URL Filter, Access Control, Local Password

ATM:	Support AAL5, UBR, VPI Range (0 ~ 255) and VCI range (1 ~ 65535), 1 PVC, OAM F4/F5 loop back.

Payload Encapsulation:

RFC2684 (RFC1483), Multi-Protocol over ATM; RFC2225 (RFC1577), IPoA

RFC2364, PPP over ATM (CHAP&PAP); RFC2516, PPPoE over ATM

LAN Port:	4x 10/100Mbps Ethernet port (RJ45), Auto-MDIX

WAN Port:	Compliant to G.dmt (G.922.1) Annex A

Compliant to G.lite (G.922.1) and T1.413 Annex A

ADSL Line Interface (RJ11)

Line Impedance: 100 Ω; Automatic-Rate Adaptation in step of 32Kbps

LEDs:	Power, Status, 10/100 (LAN 1~4), WAN

Power:	15V DC 1A External Power Adapter

Dimensions (LxWxH):	183 x 125 x 31 mm (7.2 x 4.9 x 1.2 inches)

Unit Weight:	Appr. 408 g  (0.9 lb)

Temperature:	Operating:  0˚ ~ 40˚ C (32˚ ~ 104˚ F) Storage: -20˚ ~ 70˚ C (-4˚ ~ 158˚ F)

Humidity:	Operating: 10 ~ 90% RH 	     Storage:    5 ~ 95% RH

Certifications:	FCC, CE

### TOP REASONS THE TW100-BRM504 IS A LASTING TREND

Easy Integration: With the built-in 4-port 10/100Mbps Switch, you can integrate this device to any Ethernet/Fast Ethernet Network.

Cost-Effectiveness: Share the broadband Internet connection, saves modem, router costs and account charges.

Security: Firewall protection keeps hackers out.

Performance: Experience the high speed Internet access while reducing network traffic.

Product Information

TW100-BRM504	4-Port ADSL Modem Firewall Router

TW100-BRF114	Cable/DSL 4-Port Firewall Router

TW100-BRV204	Cable/DSL VPN Firewall Router

TW100-BRV304	Cable/DSL Advanced VPN Firewall Router

TW100-S4W1CA	10/100Mbps DSL/Cable Broadband Router /w 4-port Switch

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

Sales: sales@trendware.com • Support: techsupport@trendware.com

# Text boxes

TW100-BRM504

4-Port ADSL Modem Firewall Router

TRENDnet’s TW100-BRM504 includes an ADSL Modem, SPI Firewall, Router, and 4-Port Switch ALL-IN-ONE box. Simply plug it into your DSL phone line and you have a high-performance network for your home or small office. Security includes a Stateful Packet Inspection Firewall (SPI), Denial of Service Attack prevention, VPN pass-through, and advanced Rule-Based Firewall, while the Application Level Gateway (ALG) and Port Forwarding features add flexibility so designated programs such as gaming and web-conferencing programs can work around the Firewall. Control user Internet access via URL, time, and MAC address, while Logs and reports provide monitoring of intrusion attempts and traffic. Set-up is easy with UPnP support and a Quick Install Wizard.

Network Solution for TW100-BRM504