Features

- Compliant with USB 1.1, Bluetooth 1.1 and 1.2 Specification

- Uses 2.4GHz ISM frequency band with Gaussian Frequency Shift keying (GFSK) standard

- Supports both Asynchronous Connectionless Link (ACL ) and Synchronous Connection Oriented (SCO)

- High-Speed wireless data transmission, up to 723Kbps Data Throughput in ACL mode, and up to 64 Kbps in SCO mode

- Compatible with Windows 98SE/ME/2000/XP, Mac OS X 10.2.8 or above

- Built-in 128-bit encryption for secured data communications

- Enable computers to connect Bluetooth enabled devices such as printers, Headset, Audio/Video, Basic Image, PDAs, and mobile phones

- Supports Generic Access (GAP), Service Discovery Application (SDAP), Serial Port (SPP), Dial-up Network(DUN), Fax, File Transfer (FTP), LAN Access (LAP), Synchronization (SYNC), Object Push (OPP), Generic Object Exchange (GEOP), Headset (HSP), and Hardcopy Cable Replacement (HCRP), Human Interface Device (HID) device.

- Compliant with Class I Bluetooth Operations

- Communicates wirelessly up to 100 meters (328 ft.) in limited condition

- Trouble free Plug-n-Play Installation

- 2-Year Warranty

Specifications

| Hardware |
| --- |
| Adapter Standards | USB 1.1, Bluetooth 1.1 and 1.2 |
| Antenna | 2dBi |
| Link Mode | ACL and SCO |
| TX Output | Class1 Operation |
| Supported OS | Windows 98SE/ME/2000/XP, Mac OS X 10.2.8 or above |
| Cable Length | 15cm (6in.) |
| LED Indicator | Power |
| Operating Voltage | 5V USB Power |
| Power Consumption | 80mA (Max.) |
| Temperature | Operation: 0(~ 55(C (32(F~132(F); Storage: -20(~ 55(C (-4(F~132(F) |
| Humidity | 70% (Max) |
| Dimensions | 47 x 15 x 10 mm (1.85 x 0.59 x 0.39 in.) |
| Weights | 9 g (0.3 oz.) |
| Certification | CE, FCC |
| Wireless |  |
| Frequency | 2.4 ~ 2.4835 GHz |
| Module Technique | Gaussian Frequency Shift Keying ( GFSK) |
| Output Power | +13dBm (typical) |
| Receiving Sensitivity | - 82dBm ( typical ) |
| Data Rate | Up to 723Kbps in ACL mode; up to 64Kbps in SCO mode |
| Date Range | Up to 100m (328 ft.) depends on environment |

TOP REASONS THE TBW-102UB IS A LASTING TREND

| Integration Friendly | Drivers support Windows Operating Systems |
| --- | --- |
| Economical | Save time, labor, and material for network cable installation |
| Flexible | Connects PC, Laptop, Printer, Fax, Headset, Cellular Phone, and PDA to share data, files, and information quickly and easily |
| Performance | Data Transfer Rate up to 723 kbps in ACL mode, 64 kbps in SCO mode |

Package Contents			Related Products

- TBW-102UB 				- TBW-101UB

- Quick Installation Guide

- Driver CD-ROM

- USB Cable

To order please call: 888-326-6061 • Sales: sales@trendware.com

Support: techsupport@trendware.com • Tech Support Hotline: 1(310) 626-6252

Official Site: www.TRENDnet.com

# Text boxes

TBW-102UB (v2)

High Power Bluetooth USB Adapter

Venture into the wireless realm with TRENDnet Bluetooth technology.  Enhance your PCs with Bluetooth peripherals.  Unclutter your workspace with TRENDnet’s TBW-102UB Bluetooth wireless technology.

Networking Solution with TBW-102UB