Features

- Compliant with ITU-T G.992.1 (G.dmt), G.992.2 (G.lite) and ANSI T1.413 Issue 2

- TDM-E400 is additionally compliant with ITU-T G.992.3 (G.dmt.bis / ADSL2), G.992.5 (ADSL2+) and provides up to 24 Mbps downstream rate

- Compatible and interoperable with major Central Office side ADSL DSLAM or Multi-service Access System

- One 10/100 Base-TX Ethernet port for PC / LAN connection

- RFC2684 / 1483 to bridge or route traffic over ATM over ADSL

- Support Networking protocols such as PPP, IP routing, NAPT, relay / client

- Support local and remote configuration and management through Web, Telnet or SNMP

- Simple firmware upgrade via TFTP, FTP or HTTP

- 5-Year Warranty

Specifications

| Hardware |  |
| --- | --- |
| LAN Interface | One 10/100 Base-TX Ethernet port, IEEE 802.3/3u, RJ-45 connector |
| WAN Interface (ADSL line) | One pair (2-wire) loop, 100 Ω line impedance with RJ-11 connector Compliance: ITU-T G.992.1, G.992.2 and ANSI T1.413 Issue 2 (Annex A) Compliance: ITU-T G.992.1, G.992.2, G.992.3, G.992.5 & ANSI T1.413 Issue 2 |
| Indicators | ALM (red LED) – Indicates data error or operation fault LAN (green LED) – Continuous ON when Ethernet is active; blinking while transmitting / receiving data PPP (green LED) – Continuous ON when PPP connection is established; blinking while transmitting / receiving data WAN (green LED) – Continuous ON when ADSL link is up PWR (green LED) – Continuous ON when power is properly connected |
| OAM&P | Local: Telnet or Web management via Ethernet Remote: Telnet or Web Management |
| Power | AC adapter: Input 110/220VAC, 50/60Hz; Output 15VAC 1A Power consumption: Less than 6 Watts |
| Environment | Operation Temperature and Humidity: 0°C ~ 45°C,5% ~ 95% (non-condensing) Storage Temperature and Humidity: -20°C ~ 85°C, 5% ~ 95% (non-condensing) |
| Dimensions | 170 mm ×121 mm × 36 mm (6.7 x 4.8 x 1.4 in) |
| Weight | 255g (9 oz) |
| Certifications | FCC, CE |
| Software |  |
| ATM | ATM cells over ADSL, AAL5 Supports 8 PVCs Supports UBR, CBR, rt-VBR, nrt-VBR and GFR traffic classes ADSL-aware CAC (Connection Admission Control) Support for F5 AIS, RDI, and loopback cells Payload encapsulation − RFC2684 / RFC1483, Multiprotocol Encapsulation over ATM Adaptation Layer 5 − RFC2225 / RFC1577, Classical IP and ARP over ATM(IPoA) − RFC2364, PPP over AAL5 (PPPoA) |
| Bridging | RFC2684 / RFC1483 bridged PDU encapsulation IEEE 802.1D transparent bridging and spanning tree protocol ZIPB (Zero Installation PPP Bridge) |
| Routing | RFC2684 / RFC1483 routed PDU encapsulation Supports Point-to-Point Protocol (including PPPoA and PPPoE) and user authentication via PAP or CHAP Supports TCP, UDP, ARP, RARP, IPCP, ICMP, IGMP, etc. IP routing: static route, RIP v1 and v2 NAT/PAT with extensive ALG supports DNS relay agent Layer 2 tunneling protocol (L2TP) |
| Security | Built-in firewall with protection against DOS attacks, IP spoofing, and other common types of attacks Packet filtering at MAC layer (raw filter) and IP layer, including stateful packet filtering Supports blacklist |
| Configuration and Network Management | TR037-compliant auto-configuration using ILMI SNMP v1 agent – over IP, ILMI VCC or HDLC/EOC DHCP client, server and relay for IP management Universal Plug and Play (UPnP) support Telnet with CLI (command line interface) or Web-based configuration and management FTP/TFTP or HTTP for firmware upgrade and configuration |

Package Contents							Related Products

- TDM-E400		- 1 x 1.5m (5ft) Cat.5 Cable			- TW100-BRM504

- CD-ROM (User’s Guide)	- 1 x RJ11 Telephone Cable			- TDM-C400

- Quick Installation Guide	- Power Adapter (15V AC 1A)			- TEW-435BRM

To order please call: 888-326-6061; Sales: sales@trendware.com

Support: techsupport@trendnet.com; Tech Support Hotline: (866)845-3673

Official Site: www.TRENDnet.com

# Text boxes

TDM-E400 (v2.0R)

ADSL/ADSL2+ Ethernet Modem Router

The TDM-E400 is ADSL/ADSL2+ customer premise equipment that provides high-speed asymmetrical data transmission on a single twisted copper pair. The DSL line interface supports various ADSL standards, up to ADSL2+. At the DTE side these CPEs provide one 10/100 Ethernet interface for easy connection to user’s PC or LAN environment. TDM-E400 delivers broadband access for enterprises, telecommuters, home, and remote office workers with high-speed data transfer requirements.

TDM-E400

Network Solution for TDM-E400