Features

- Compliant with USB 2.0 High-Speed Printing

- One RJ-45 10/100Mbps Auto-MDIX Fast Ethernet Port

- Includes LPR Program for Windows 95/98/ME TCP/IP Printing

- Supports IPP Printing for Windows 2000/XP

- Supports second HTTP port for Remote Web Configuration and IPP Printing

- Supports Mac 10.2 “Rendezvous” Zero-Configuration Function

- TCP/IP protocol supports DHCP, IPP, LPR, HTTP

- Includes Windows-Based Administrative Program and Web-Based Configuration

- Built-in Flash Memory for Easy Firmware Upgrade

- 5-Year Warranty

*Mac Systems are only compatible with Post-Script printers

Specifications

| Hardware |
| --- |
| Standards | IEEE 802.3 10Base-T IEEE 802.3u 100Base-TX |
| Printer Interface | USB 2.0, 1.1 Compliant USB Type A Port |
| LAN Port | 10/100Mbps Auto-MDIX Ethernet Port |
| CPU/ SDRAM / Flash ROM | RDC R2886 150MHz / 2MByte / 512KByte |
| Diagnostic LED | Power, USB, LAN |
| Transport Protocol | TCP/IP |
| TCP/IP Protocol Supported | DHCP, IPP, LPR, HTTP |
| OS Support | Windows 95/98(SE)/ME/NT/2000/XP/2003 Netware 5.x NDPS LPR Remote Printing (TCP/IP) Unixware, Linux Mac OS X (IP Printing) |
| Management | PS Utility or Web-Browser Configuration |
| Power | 5V DC 2.5A External Power Adapter |
| Dimensions | 115 x 85 x 30mm (4.5 x 3.4 x 1.2 inches) |
| Weight | 128g (4.5oz.) |
| Temperature | Operating: 0(C~50(C (32(F~122(F) Storage: -25(C~55(C (-13(F~131(F) |
| Humidity | 10%~90% (non-condensing) |
| Certification | CE, FCC |

Package Contents							Related Products

- TE100-P1U								- TE100-P21

- Multi-Language Quick Installation Guide				- TEW-P1PG

- Utility & User’s Guide CD-ROM					- TEW-P21G

- Power Adapter (5V DC, 2.5A)

To order please call: 888-326-6061; Sales: sales@trendnet.com

Support: support@trendnet.com; Tech Support Hotline: 866-845-3673

Official Site: www.trendnet.com

# Text boxes

Network Solution for TE100-P1U

10/100Mbps USB 2.0 Print Server

TRENDnet’s TE100-P1U is a print server that transforms any stand-alone USB  printer into a shared network printer. The TE100-P1U provides Fast Ethernet interface for integrating into existing network. The TE100-P1U is designed for printers equipped with USB 2.0 compliant printer port and it is an ideal network solution to convert conventional USB printer into a shared resource on the network.

TE100-P1U (Version V2.1R/V2.2R)