FEATURES

- 24 10/100Mbps Auto-negotiation, Auto-MDIX Fast Ethernet Ports

- 1 module slot for optional multi-mode (2Km) or single-mode (15Km) 100Base-FX SC fiber module

- Full/Half-Duplex transfer mode for each port

- Full wire-speed Non-Blocking reception and transmission

- Store and Forward switching method

- 768K bytes RAM data buffer and 4K entries MAC address table

- Extensive diagnostic LED’s on the front panel

- IEEE 802.3x flow control for full-duplex mode; Back Pressure flow control for half-duplex mode

- Easy configuration via Web browser

- Proprietary Windows Based Management/Monitoring Utility (similar to SNMP Trap)

- Port-Based VLAN (25 groups) and Port-Based IEEE 802.1p QoS (High/Normal)

- Port Setting function, users can set each port’s availability, speed, duplex mode, and flow control

- Standard 19” Rack-mount design

- 5-Year Warranty

# TECH SPEC’S

LAN Standards:	      	IEEE 802.3 10Base-T; IEEE 802.3u 100Base-TX, 100Base-FX

Network Media:	     	Ethernet: UTP/STP Cat. 3, 4, 5. 100 meters max.

Fast Ethernet: UTP/STP Cat. 5. 100 meters max.

Optional Fiber Module:	50/125 or 62.5/125um multi-mode fiber, 2Km max.

9/125 or 10/125um single-mode fiber, 15Km max.

Protocol:			CSMA/CD

Topology:			Star

LAN Port:			24 x 10/100Mbps Auto Negotiation, Auto-MDIX ports,

1 x module slot for optional 100Base-FX fiber module with SC connector

Address Table:	      	4K entries per device

Data Transfer Rate:	Ethernet: 10/20Mbps (Half/Full-Duplex)

Fast Ethernet: 100/200Mbps (Half/Full-Duplex)

Backplane:	2.7Gbps

Total Throughput:	5.0Gbps (with the optional fiber module)

Diagnostic LEDs:		Per Unit: Power, System, Per Port (RJ-45): Link/Activity, 100Mbps.

FX (optional fiber module): Link/Activity, FDX

Power Consumption:      	14 Watts. Max

Dimensions (WxHxD):     	440 x 140 x 44 mm (17.32 x 5.5 x 1.73 inches)

Weight:			2Kg. (4.48 lb)

Operating Temperature:  	0( ~ 40( C (32( ~ 104( F)

Storage Temperature: 	-10( ~ 70( C (14( ~ 158( F)

Humidity:	10% ~ 90% (no-condensing)

Certifications:	FCC Class A, CE Mark A, VCCI-A

TOP REASONS THE TE100-S24WS IS A LASTING TREND

Easy Installation: 	Each RJ-45 port auto-senses connection speed, duplex type and MDI-X media type. Connect to 10 or 100Mbps network devices with straight through or crossover cable.

Expandability: 	Expand the connection up to 15Km with optional single-mode SC-Type fiber module.

Flexibility: 	Easy configuration and management through Web Browser.

Performance:            	Non-blocking high performance with internal Switch Controller.

Cost-Effectiveness:   	Provides Fast Ethernet Switch with management functions at an affordable price.

TE100-S24WS	24-Port 10/100Mbps web-based Smart Switch with Fiber Slot (Rack Mount)

TE100-S16V	16-Port 10/100Mbps Smart Switch with Fiber Slot (Rack Mount)

TE100-S24V	24-Port 10/100Mbps Smart Switch with Fiber Slot (Rack Mount)

TE100-SFXM	SC-type multi-mode 2Km fiber slide-in module for Smart Switch

TE100-S15M	SC-type single-mode 15Km fiber slide-in module for Smart Switch

## To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

Sales: sales@trendware.com • Support: techsupport@trendware.com ss08132003

# Text boxes

Product Information

TE100-S24WS

24-port 10/100Mbps Web-Based Smart Switch

TRENDnet's TE100-S24WS 24-port 10/100Mbps Web-Based Smart Switch is the ideal Switch for network segmenting.  It has 24 10/100Mbps Auto-Sensing and Auto-MDIX ports for easy installation. The Switch also has a module slot that accepts optional single- or multi-mode 100Based-FX fiber module for connection up to 15Km. TE100-S24WS supports web browser configuration; Network Administrator can use web browser to configure port speed, port-based VLAN and QoS, and also monitor each port’s status. TRENDnet's TEW100-S24WS is powerful and easy-to-use in reducing unnecessary broadcast traffic and enhance network security.

Network Solution for TE100-S24WS