Features

- 32 x 10/100Mbps Auto Negotiation and Auto-MIDX ports

- 1 Module Bay for Optional 100Base-FX SC Type Connector Fiber Module

- Full/Half Duplex Transfer Mode for Each Port

- Store and Forward Switching Method

- Integrate Address Look-Up Engine, Supports 4K Absolute MAC Address

- Supports 1M Bytes RAM for Data Buffering

- Extensive Front Panel Diagnostic LEDs

- Broadcast Storm Protection

- IEEE 802.3x Flow Control for Full-Duplex Mode

- Backpressure Flow Control for Half-Duplex Mode

- Standard 19” Rack-Mount Design

- 5-Year Warranty

Specifications

| Hardware |
| --- |
| Standards | IEEE 802.3 10Base-T IEEE 802.3μ 100Base-TX ANSI/IEEE 802.3 Auto-Negotiation |
| Protocol | CSMA/CD |
| Topology | Star |
| Connectors | 32 x10/100Mbps Auto-MDIX RJ45 Ports 1 x 100Base-FX Fiber Module Slot for Optional Fiber Adapter (TE100-SFXM) |
| Cabling | Cat. 3,4,5 UTP/STP for 10Base-T Cat. 5 UTP/STP for 100Base-TX 62.5/125u Multimode Fiber/SC Type Connector for 100Base-FX |
| Data Transfer Rate | 10Mbps: 10/20Mbps (Half/Full Duplex) 100Mbps: 100/200Mbps (Half/Full Duplex) |
| Data Range | 10Mbps: max 100 meters 100Mbps: max 100 meters 100Base-FX: max 2KM |
| Data RAM Buffers | 1MB per device |
| Filtering Address Table | 4K Entries Per Device |
| Diagnostic LEDs | Power, 10/100Mbps Link/Activity, Collision/Full Duplex, FX |
| Power | 100 ~ 240VAC 50/60Hz, Internal Universal Switching Power |
| Power Consumption | 40 Watts (Max) |
| Dimensions (W x H x D) | 440mm x 200mm x 44mm (17.3” x 7.9” x 1.73”) |
| Weights | 3.0 Kg (6.6 lb) |
| Temperature | Operating: 0(C ~ 40(C (32(F ~ 104(F) Storage: -10(C to 70(C (14(F to 158(F) |
| Humidity | Operating: 10 % ~ 90 % (non-condensing) Storage: 5 % ~ 90 %(non-condensing) |
| Certifications | FCC, CE |

TOP REASONS THE TE100-S32plus IS A LASTING TREND

| Integration Friendly | Easily upgrade to Fast Ethernet without changing switch |
| --- | --- |
| Economical | Provides 10/100Mbps of Fast Ethernet in the same unit |
| Flexible | All Ports automatically negotiate 10/100 network speed, half/full modes, and Auto-MDIX connector type |
| Performance | Supports store and forward switching architecture with non-blocking full wire-speed performance |

Package Contents	Related Product

- TE100-S32plus					- TE100-S16

- Multi-Language User’s Guide				- TE100-S24

- Power Cord						- TE100-SFXM

- Rack Mount Kit

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

### Sales: sales@trendware.com • Support: techsupport@trendware.com

Tech Support Hot Line: (310)626-6252

### Official Site: www.TRENDNET.com

# Text boxes

Front View

Network Solution for TE100-S32plus

32-Port 10/100Mbps Fast Ethernet Switch

TRENDnet’s TE100-S32plus is a high performance, auto-sensing 32-port rack-mountable Fast Ethernet Switch. It is designed to eliminate unnecessary traffic and relieve congestion on critical network paths.  It automatically negotiates between 10/100Mbps network speed and half/full duplex modes.

TE100-S32plus