Features

- Compliant with IEEE 802.3 and IEEE 802.3μ standards

- 8 10/100Mbps Auto-Negotiation and Auto-MDIX Fast Ethernet Ports

- Half or Full Duplex Operation for Each Port

- Operates at Maximum Packet Filtering and Forwarding Rate

- Store and Forward Switching Method

- 256KB Buffer memory

- Address Table up to 8K MAC Address

- Compact Design with External Power Adapter

- Comprehensive LED indicators for Port Status

- Stackable Design with Stacking Kit included

- 5-Year Warranty

Specifications

| Standards: | IEEE 802.3 for 10Base-T Ethernet IEEE 802.3μ for 100Base-TX Fast Ethernet. ANSI/IEEE 802.3 Auto-Negotiation |
| --- | --- |
| Data Transfer Rate: | 10/100Mbps (20/200Mbps in full-duplex mode) |
| Protocol: | CSMA/CD |
| Connectors: | 8 UTP/STP RJ-45 Auto-MDIX |
| Network Media: | UTP EIA/TIA-568 CAT 3, 4, 5 (max. 100m) for 10Base-T UTP EIA/TIA-568 CAT 5 (max. 100m) for 100Base-TX |
| Packet Forwarding Rate: | 10Base-T: 14,880pps per port (half-duplex) 100Base-TX: 148,800pps per port (half-duplex) |
| Topology: | Star |
| Diagnostic LEDs: | Power, Link/Activity |
| Power: | External power supply 7.5V, 1A Consumption: 2 watts (max) |
| Dimensions: | 165 x 114 x 44 mm (6.5 x 4.5 x 1.7 inches) |
| Weight: | Appr. 236g (0.52lb) |
| Operating Temp: | 0˚ to 50˚ C (32˚ F to 122˚ F) |
| Storage Temp: | -10˚ to 70˚ C (14˚ F to 158˚ F) |
| Operating Humidity: | 10 % to 90 % RH |
| Storage Humidity: | 5 % to 90 % RH |
| Certifications: | FCC, CE |

| Easy Installation | Designed to link 10Mbps and 100Mbps networks |
| --- | --- |
| Flexibility | Auto-Negotiation and Auto-MDIX Ports for Easy Uplink |
| Expandability | All ports support 200Mbps (in full-duplex mode), expandable from any port and for any number of Switches |
| Easy Migration | Easy upgrade to Fast Ethernet without reconfiguring existing network |
| Dependability | Parallel store-and-forward architecture allows direct transfer |

TE100-S8P	8-Port 10/100Mbps Auto-MDIX Fast Ethernet Mini Switch

TE100-S5P	5-Port 10/100Mbps Auto-MDIX Fast Ethernet Mini Switch

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

sales@trendware.com • techsupport@trendware.com    www.TRENDnet.com

# Text boxes

Network Solution for TE100-S8P

PRODUCT

INFORMATION

TE100-S8P(B1)

## 8-Port 10/100Mbps Auto-MDIX

## Fast Ethernet Mini Switch

TRENDnet’s TE100-S8P, 8-port, palm-sized 10/100Mbps Fast Ethernet Switch, presents the perfect choice for small workgroups for any desktop space.  It allows users to simply plug any port to either a 10Mbps or 100Mbps network to multiply bandwidth, boost response time and satisfy heavy load demands. The ports automatically negotiate between 10Base-T and 100Base-TX network speeds, half- and full-duplex modes, and MDI-II and MDI-X media types.  TE100-S8P is truly a Plug-N-Play device, which provides cost-effective and high-performance solutions.

Front Panel

Back Panel

# TOP FIVE REASONS THE TE100-S8P IS A LASTING TREND