FEATURES

- 24 10/100Mbps Auto-negotiation MDIX Fast Ethernet Ports

- 2 10/100/1000Mbps Auto-negotiation, Auto-MDIX Gigabit Ports

- 2 mini GBIC ports for optional LC type gigabit fiber module

- Full/Half duplex mode for each port

- Store and Forward switching method

- Integrated address Look-Up Engine with 4K absolute MAC address table

- Supports 768K bytes RAM data buffering

- Extensive diagnostic LED’s on the front panel

- IEEE 802.3x flow control for full-duplex mode

- Back pressure flow control for half-duplex mode

- Easy configuration the device from a Web browser

- Supports Port-Based VLAN (28 groups) and Port-Based IEEE 802.1p QoS (High/Normal)

- Supports Trunking (gigabit ports) and Port Mirroring

- Support Port setting function allow user setting each port’s speed, duplex mode, and flow control

- Standard 19” Rack-mount design

- 5-Years Warranty

# TECH SPEC’S

LAN Standards:	IEEE 802.3 10Base-T, IEEE 802.3u 100Base-TX, IEEE 802.3ab 1000Base-T, IEEE 802.3z 1000Base-SX/LX (mini GBIC). IEEE 802.3x Full Duplex Flow Control

Network Media:	     		Ethernet: UTP/STP Cat. 3, 4, 5

Fast Ethernet: UTP/STP Cat. 5

Gigabit : UTP/STP Cat. 5

Protocol:				CSMA/CD

Topology:			Star

LAN Port:		24 x 10/100Mbps Auto Negotiation, Auto-MDIX Fast Ethernet ports,

2 x 10/100/1000Mbps Auto Negotiation, Auto MDIX Gigabit ports

2 x mini GBIC ports

Address Table:	      		4K entries per device

Data RAM buffer			768 KB per device

Data Transfer Rate:		Ethernet:  10/20Mbps – Half/Full-Duplex

Fast Ethernet:  100/200Mbps – Half/Full Duplex

Gigabit Ethernet: 2000Mbps – Full Duplex

Diagnostic LEDs:			Per Unit: Power System

Per Fast Ethernet Port: Link/ACT, 100M

Per Gigabit Ethernet Port: Link/ACT, 1000M, 100M

Per GBIC Gigabit Port: Link/ACT, 1000M

Power Consumption:      		19 Watts. Max

Power Supply:			100-240V AC, 50/60Hz Internal Universal Power Supply

Dimensions:     			440 x 200 x 44 mm (17.32"  x 7.9" x 1.73")

Weight:				5.78 lb

Operating Temperature:  		0( ~ 40( C (32( ~ 104( F)

Storage Temperature: 		-10( ~ 70( C (14( ~ 158( F)

Humidity:		10% ~ 90% (no-condensing)

Certifications:		FCC Class A, CE Mark A, VCCI-A

TOP REASONS THE TEG-2224WS IS A LASTING TREND

Easy Upgrade: 	Ethernet workgroups are able to upgrade to Fast Ethernet by changing adapters and a hub without changing switches.

Expandability: 	Expand the connection distance with optional GBIC fiber modules.

Flexibility: 	Easy management and configuration through Web browser

Performance:            	Provides non-blocking high performance with internal switch controller.

Cost-Effectiveness:   	The TEG-2224WS presents Gigabit Ethernet at an affordable rate.

TEG-2224WS	28-Port 10/100/1000Mbps Web-Based Gigabit Smart Switch (Rack Mount)

TE100-S24WS	24-Port 10/100Mbps Smart Switch with Fiber Slot (Rack Mount)

TE100-S16V	16-Port 10/100Mbps Smart Switch with Fiber Slot (Rack Mount)

TE100-SFXM	SC-type fiber slide-in module for TE100-S16V/S24WS

## To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • TEL: (310) 891-1100 • Fax: (310) 891-1111

Sales: sales@trendware.com • Support: techsupport@trendware.com

# Text boxes

Product Information

TEG-2224WS

28-port 10/100/1000Mbps Gigabit

Web-Based Smart Switch

TRENDnet's TEG-2224WS 10/100/1000Mbps Web-Based Smart Gigabit Switch is the ideal Switch for network segmenting. It has 24 10/100Mbps, 2 10/100/1000Mbps Auto-Sensing and Auto-MDIX RJ45 ports for easy installation. And this Switch also has 2 additional mini GBIC ports that accept optional gigabit fiber modules for great flexibility. TEG-2224WS supports web browser configuration; Network Administrator can use web browser to configure port speed, port-based VLAN, QoS, Trunking and also monitor each port’s status. TRENDnet's TEG-2224WS is powerful and easy-to-use in reducing unnecessary broadcast traffic and enhance network security.

Network Solution for TEG-2224WS

Optional Module

- TEG-MGBSX

- TEG-MGBS10

- TEG-MGBS30

- TEG-MGBS50

- TEG-MGBS70