Features

- 48 x 10/100Mbps Auto-Negotiation and Auto-MDIX Fast Ethernet Ports

- 2 x 10/100/1000Mbps Auto-Negotiation and Auto-MDIX Gigabit Ports

- 2 x Mini-GBIC ports for optional LC type Gigabit Fiber Module

- Full/Half-Duplex Transfer Mode for each Port (only Full Duplex Mode for 1000Mbps)

- Store and Forward Switching Architecture

- Integrated address Look-Up Engine with 4K absolute MAC address table

- Supports 1536K bytes RAM Data Buffering

- IEEE 802.3x Flow Control for Full Duplex Mode

- Back Pressure Flow Control for Half Duplex Mode

- Supports 2 groups of Port-Based VLAN (up to 28 groups) * and Port Trunking

- Supports Port-Based IEEE 802.1p QoS (High/Normal)

- Port Settings function, users can set each Port’s Availability, Speed, Duplex mode and Flow Control

- Easy Window Based Management Utility and Web-Based Configuration

- Extensive Diagnostic LED’s on the front panel

- Standard 1U (19”) Rack-Mount Size (Rack-Mount Kit included)

- 5-Year Warranty

* Port Based VLAN and QoS limited to One Group. Group 1 (Ports 1 - 24) or Group 2 (Ports 25 - 52)

Specifications

| Standards | IEEE 802.3 10Base-T, IEEE 802.3u 100Base-TX IEEE 802.3ab 1000Base-T, IEEE 802.3z 1000Base-SX/LX IEEE 802.3x Full Duplex Flow Control |
| --- | --- |
| Network Media | Ethernet: UTP/STP Cat. 3, 4, 5 Fast Ethernet: UTP/STP Cat. 5 Gigabit: UTP/STP Cat. 5 |
| Protocol /Topology | CSMA/CD, Star |
| LAN Ports | 48 x 10/100Mbps Auto Negotiation, Auto-MDIX Fast Ethernet ports 2 x 10/100/1000Mbps Auto Negotiation, Auto MDIX Gigabit ports 2 x Mini GBIC ports for optional Mini-GBIC modules |
| Data Transfer Rate | Ethernet: 10Mbps/20Mbps (Half-Duplex/Full-Duplex) Fast Ethernet: 100Mbps/200Mbps (Half-Duplex/Full-Duplex) Gigabit Ethernet: 2000Mbps (Full-Duplex) |
| Address Table | 4K Entries |
| Data RAM Buffer | 1536KBytes |
| Diagnostic LEDs | Per Unit: Power, System Per Fast Ethernet: Link/ACT Per Cooper Gigabit Port: Link/ACT, Speed (1000M-Green, 100M-Amber) Per Mini-GBIC Gigabit Port: Link/ACT |
| Power/Consumption | 100-240V AC, 50/60Hz Internal Universal Power Supply / 24 watts (max) |
| Dimensions (W x D x H) | 440 x 200 x 44 mm (17.32" x 7.9" x 1.73") |
| Weight | 2.6kg (5.78lbs) |
| Temperature | Operating : 0( ~ 40( C (32( ~ 104( F) Storage: -10( ~ 70( C (14( ~ 158( F) |
| Humidity | 10% ~ 90% (no-condensing) |
| Certifications | FCC Class A, CE Class A |

TOP REASONS THE TEG-2248WS IS A LASTING TREND

| Easy Upgrade | Ethernet workgroups are able to upgrade to Fast Ethernet by changing adapters and a hub without changing switches |
| --- | --- |
| Expandability | Expand the connection distance with Mini-GBIC connections |
| Flexibility | Connects to 10Base-T, 100Base-TX, and 1000Base-T Networks |
| Performance | Provides non-blocking high performance with internal switch controller |
| Cost-Effectiveness | The TEG-2248WS presents Gigabit Ethernet at an affordable rate |

TEG-2248WS	52-Port Gigabit Web-Based Smart Switch

TEG-160WS	16-Port Gigabit Web-Based Smart Switch

TEG-240WS	24-Port Gigabit Web-Based Smart Switch

## To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • TEL: (310) 891-1100 • Fax: (310) 891-1111

Sales: sales@trendware.com • Support: techsupport@trendware.com

www.TRENDNET.com

# Text boxes

Product Information

TEG-2248WS

52-Port Gigabit Web-Based Smart Switch

TRENDnet's TEG-2248WS 52-port Gigabit Web-Based Smart Switch is the ideal switch for network segmenting. It has 48 10/100Mbps and 2 10/100/1000Mbps RJ45 ports with Auto-Sensing and Auto-MDIX feature for easy installation. This switch also has 2 Mini-GBIC ports that accept optional gigabit fiber modules for greater flexibility. The TEG-2248WS supports web browser configuration; Network Administrators can use web browsers to configure port speed, port-based VLAN, QoS, Trunking and also to monitor each port's status. TRENDnet's powerful and easy-to-use TEG-2248WS is designed to reduce unnecessary broadcast traffic and enhance network security.

Network Solution for TEG-2248WS

Optional Module

- TEG-MGBSX

- TEG-MGBS10

- TEG-MGBS30

- TEG-MGBS50

- TEG-MGBS70