FEATURES

- IEEE 802.3, 802.3u and 802.3ab compliant

- Support 32/64-Bit 33/66Mhz PCI Local Bus Master high-speed operation of Rev. 2.1/2.2 specification

- One RJ-45 Connector:  Auto connection speed detection of 10Mbps Ethernet, 100Mbps Fast Ethernet, and 1000Mbps Gigabit Ethernet

- Auto MDI-X/MDI-II medium type detection

- Supports Full-Duplex mode doubles the bandwidth to 20/200/2000Mbps

- Built-in FIFO buffers reduces overhead of memory transfers

- Plug and Play Installation

- 5-years warranty

TREND SPEC’S

Standards: 			IEEE 802.3 10Base-T Ethernet, IEEE 802.3u 100Base-TX Fast Ethernet

IEEE 802.3ab 1000Base-T Gigabit Ethernet, ANSI/IEEE 802.3 NWay Auto-Negotiation, IEEE 802.X Flow Control

Data Transfer Rate: 		Ethernet:  10Mbps (Half-Duplex) 20Mbps (Full-Duplex)

Fast Ethernet 100mbps (Half-Duplex), 200Mbps (Full-Duplex)

Gigabit Ethernet 1000Mbps (Half-Duplex), 2000Mbps (Full-Duplex)

Cabling:			Ethernet: 2-pair UTP CAT 3,4,5, EIA.ITA-568 100-ohm screened twisted pair (STP)

Fast Ethernet: 2-pair UTP CAT 5, EIA/TIA-568 100ohm screened twisted pair (STP)

Gigabit Ethernet: 4-pair UTP CAT 5, EIA/TIA-568 100-ohm screened twisted pair (STP)

Host Interface: 		32/64-bit 33/66Mhz PCI Rev.2.1/2.2

Connector:			Single RJ-45 UTP/STP, Auto MDI-II/MDI-X

Diagnostic LEDs:		10 Link, 100 Link, 1000 Link, Full-Duplex, Collision, and Activity

Power Consumption:	10 Watts (max)

Driver Support:	Windows 98/Me/2000/NT4.0, Linux, Novell Netware Server 5.x, and more

Dimensions:			164 x 69 mm (W x H)

Weight:			120.5g (4.25 Oz)

Operating Temp.:		-10( to 50( C (14( to 122(F)

Storage Temp.:		-10( to 70( C (14(  to 158(F)

Operating Humidity:		10 % to 90 % non-condensing

Storage Humidity:		5% ~ 90% non-condensing

Certifications:		FCC Class B, CE Class B, VCCI Class B

TOP REASONS THE TEG-PCITX2 IS A LASTING TREND

Performance: 	The full-duplex Gigabit adapter brings high bandwidth with 2000Mbps speeds

User Friendliness:	Plug and Play with drivers support all popular network operating systems.

Flexibility:	Single RJ-45 connector auto detects 10/100/1000Mbps connection speed, Half/Full duplex mode, and MDI-II/MDI-X medium type.

Cost-Effectiveness:	Provides the benefit of Gigabit Ethernet networking with the familiarity of Ethernet that operates in existing 32-bit PCI Bus.

TEG-PCITX2	32/64-Bit PCI 10/100/1000Mbps NWay Copper Gigabit Ethernet Adapter

TEG-PCITX	32-Bit PCI 10/100/1000Mbps NWay Copper Gigabit Ethernet Adapter

TEG-S18TX	9-port 10/100/1000Mbps NWay Copper Gigabit Switch

TEG-S224TX	26-port 10/100/1000Mbps NWay Copper Gigabit Switch

TEG-S80TX	8-port 10/100/1000Mbps NWay Copper Gigabit Switch

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

Sales: sales@trendware.com • Support: techsupport@trendware.com

# Text boxes

TEG-PCITX2

PRODUCT

INFORMATION

TEG-PCITX2

Gigabit Ethernet Card Solution

32/64-Bit PCI 10/100/1000Mbps NWay

Copper Gigabit Ethernet Adapter

TRENDnet’s TEG-PCITX2 32/64-Bit PCI 1000Base-T NWay Copper Gigabit Ethernet Card is a   high-bandwidth network adapter that auto-senses 10/100/1000Mbps connection speed, half/full-duplex mode, and MDI-X/MDI-II medium type.  It includes the latest VLAN and multicasting functions to efficiently utilize network bandwidth for maximum data throughput.  With its 1000Mbps bandwidth capacity, the TEG-PCITX2 is ideal for high traffic Power Server and Video-Conferencing Workstation.