## Features

- Support 32-Bit PCI Local Bus Master high-speed operation of Rev. 2.3 specification

- 1 x 10/100/1000Mbps Auto Negotiation and Auto MDI-X Gigabit Port

- Built-in FIFO (8K/64K) buffers reduce overhead of memory transfers

- Supports Full-Duplex Mode Doubles Network Data Rate to 20/200/2000Mbp

- Supports IEEE 802.1Q VLAN Tagging (Windows 2000 and above only)

- Supports Wake-on-LAN for Remote Wake up

- Supports Windows 98SE/ME/2000/XP/Vista Operating Systems

- Plug and Play

- 5-Years Warranty

Specifications

| Hardware |
| --- |
| Standards | IEEE 802.3 10Base-T Ethernet IEEE 802.3u 100Base-TX Fast Ethernet IEEE 802.3ab 1000Base-T Gigabit ANSI/IEEE 802.3 Auto-Negotiation |
| Network Media | Ethernet: UTP Cat. 3, 4, 5, EIA/TIA-568 100-ohm STP Fast Ethernet: UTP Cat. 5, EIA/TIA-568 100-ohm STP Gigabit: UTP Cat. 5, 5E, 6 EIA/TIA-568 100-ohm STP |
| Protocol | CSMA/CD |
| Interface | 32-Bit 33/66Mhz PCI Rev 2.1/2.2/2.3 |
| Power Consumption | 3.7watts |
| Diagnostic LED | Link/Activity |
| Supported OS | Windows 98/ME/NT4.0/2000/XP/2003/Vista Novel NetWare Server 5.x / 6.x Linux Kernel 2.4.x / 2.6.x |
| Data Rate | Ethernet: 10Mbps/20Mbps (Half/Full-Duplex) Fast Ethernet: 100Mbps/200Mbps (Half/Full-Duplex) Gigabit: 2000Mbps(Full Duplex) |
| Dimension | 120 x 59 x 15 mm (4.7 x 2.3 x 0.6 inch) |
| Temperature | Operating: 0° ~ 40° C (32° ~ 104° F) Storage: -10° ~ 70° C (14° ~ 158° F) |
| Humidity | Operating: 10%~90% (Non-Condensing) Storage: 5%~90% (Non-Condensing) |
| Certification | CE, FCC |

Package Contents

- TEG-PCITXR

- Multi-Language Quick Installation Guide

- Driver CD-ROM

##### To order please call: 888-326-6061

20675 Manhanttan Place • Torrance, CA 90501 • (310) 961-5500 • Fax: (310) 961-5511

Sales: sales@trendnet.com • Support: techsupport@trendnet.com

Tech Support Hotline: (310) 626-6252

Official Site: www.TRENDnet.com

# Text boxes

TEG-PCITXR (v3.0R)

10/100/1000Mbps Gigabit PCI Adapter

TEG-PCITXR 32-bit 10/100/1000Mbps Copper Gigabit Ethernet adapter is a high-bandwidth network adapter that auto-senses 10/100/1000Mbps connection speed, half/full-duplex modes, and MDI-X media type. It includes the latest VLAN tagging to efficiently utilize network bandwidth for maximum data throughput.  With its 2000Mbps bandwidth capacity, TEG-PCITXR is ideal for high traffic Power Server and Video-Conferencing Workstation.

Related Products

- TEG-S50TXE

- TEG-S80TXE

- TEG-PCBUSR