Features

- 16 10/100/1000Mbps Auto-Negotiation and Auto-MDIX ports

- Full/Half Duplex Transfer Mode for Each Port (1000Base-T connections support full-duplex mode only)

- Store and Forward Switching Method

- High Performance Single-Chip Design

- Non-Blocking Wire Speed Reception and Transmission

- IEEE 802.3x Full-Duplex Flow Control

- Integrated Address Look-Up Engine, Supports 8k Absolute MAC Address

- 340KBytes RAM Data Buffering

- Extensive Front Panel Diagnostic LEDs

- Standard 19” Rack-Mount Size

- 5-year Warranty

## Specifications

| Hardware |
| --- |
| Standards | IEEE 802.3 10Base-T IEEE 802.3u 100Base-TX IEEE 802.3ab 1000Base-T IEEE 802.3x Full Duplex Flow Control |
| Network Media | Ethernet: 2-pair UTP Cat. 3, 4, 5, up to 10Mbps Fast Ethernet: 2-pair UTP Cat. 5, up to 100Mbps Gigabit: 4-pair UTP Cat. 5, 5E, 6, up to 1000Mbps |
| Transmission Method | Store-and-Forward |
| Transfer Rate | Ethernet: 10Mbps/20Mbps (Half/Full Duplex) Fast Ethernet: 100Mbps/200Mbps (Half/Full Duplex) Gigabit: 2000Mbps (Full Duplex) |
| Switch Fabric | 31Gbps Forwarding Capacity |
| Data RAM Buffer | 340Kbytes |
| MAC Table | 8K entries per device |
| LED | Per Unit: Power Per Port: Link/ACT, 1000M, 100M |
| Power | 100~240V AC, 50/60Hz, Internal Power Supply |
| Power Consumption | 13.5 watts. (max) |
| Dimensions | 440 x 140 x 44 mm (17.3 x 5.5 x 1.73 inch) |
| Weight | 3Kg (6.6 lb) |
| Temperature | Operating: 0( ~ 40( C (32( ~ 104(F) Storage: -10( ~ 70( C (14( ~ 158(F) |
| Humidity | 10% ~ 90% (non-condensing) |
| Emissions | FCC, CE |

Related Products					Package Contents

- TEG-PCBUSR					- TEG-S160TX

- TEG-PCITXR						- Multi-Language Quick Installation Guide

- TEG-S240TX						- Rack Mount Kit

- Power Cord

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

Sales: sales@trendnet.com • Support: techsupport@trendnet.com

Official Site: www.TRENDnet.com

# Text boxes

TEG-S160TX (ver. D1.0R)

#### 16-Port 10/100/1000Mbps Copper Gigabit Switch

#### TEG-S160TX is a high performance 16-port rack mountable Copper Gigabit Switch. With auto-negotiation technology, the TEG-S160TX automatically negotiates between 10Base-T, 100Base-TX and 1000Base-T network speeds, as well as half and full duplex modes.  The Auto-MDIX feature on each port automatically detects and adjusts connection type with either straight-through or crossover cable.  Providing simple migration, scalability, and flexibility to handle new applications and data types, TEG-S160TX is a highly reliable and cost effective solution for high-speed network applications.