Features

- Stackable up to 16 Switches with Gigabit Ports

  - Single IP function supports up to 32 Switches

  - Single IP management with stackable mode (Gigabit ports only)

  - Single IP management with agent mode (Any port on the switch)

- Manage all Uplink or Stacked Switches Locally or Remotely with a Single IP Address

  - Public IP required when managing remotely; Port 80/28019 need to be opened when running behind a Firewall/Router

- 24 10/100Mbps Auto-Negotiation and Auto-MDIX Fast Ethernet Ports

- 2 Pairs of 10/100/1000mbps Gigabit Copper Port and Mini-GBIC Slot (1 Copper +  1 Mini-GBIC slot per pair)

- Built-in 3Mb Packet Buffer and 1Mb Control Buffer

- Provides 6K MAC, 4K VLAN and 2K Multicast Entries

- Supports 255 Entries of Static MAC and Port Based MAC Table Display

- Supports 802.3x Flow Control for Both Half/Full Duplex Operation

- Supports Head-of-Line Blocking Prevention

- Supports Broadcast Storm Filtering

- Supports Port-Based VLAN (256 Groups), IEEE 802.1Q Tag-Based VLAN (PVID 1~255)

- Supports 802.1v Protocol-Based VLAN Classification

- Supports 802.1x Authentication and Authorization

- Supports IP Multicast, IGMP Snooping and 802.1D Spanning Tree

- Supports 2-Level Priority Queuing

- Supports Port Trunking with Flexible Load Distribution Control and Fail-Over Functions

  - Max 7 Trunk groups with 4 ports per group

- Supports Ingress Port Security Mode and By-Port Egress/Ingress Rate Control

- Supports Source-Port-Based, Destination-Port-Based, and Source-Destination-Pair-Based Sniffer Function

- Supports RMON Group 1, 2, 3, 9 and PING Function from the Switch

- Store-and-Forward Switching Architecture with Non-Blocking Wire-Speed Performance

- Configuration via Console Port (serial cable included), SNMP (v1.0, MIB II), TELNET, and Web Browser

- Upgradable Firmware via Browser with TFTP Program

- Standard 19” (1U) Rack Mount Size (kit included)

- 5-Year Warranty

Specifications

| Hardware |
| --- |
| Standards | IEEE 802.3 10Base-T Ethernet IEEE 802.3u 100Base-TX Fast Ethernet IEEE 802.3z 1000Base-SX/LX Gigabit Ethernet IEEE 802.3x Flow Control IEEE 802.1D Spanning Tree IEEE 802.1q Tag-based VLAN, Priority Control IEEE 802.1v Protocol-Based VLAN IEEE 802.1x Authentication and Authorization IEEE 802.3ad Link Aggregation |
| Interfaces | 24 x 10/100Mbps Auto-MDIX RJ45 Fast Ethernet Port 2 pairs x 1000-Based RJ45 Port and Mini-GBIC Slot* 1 x RS-232 Serial Port (Initial Setup) * One RJ45 Port or Mini-GBIC Slot of each pair can be used at a time. |
| Packet Forwarding and Filtering Rate | 1000M Ethernet: 1,488,000 packets per second per port 100M Ethernet: 148,800 packets per second per port 10M Ethernet: 14,880 packets per second per port |
| Cabling | Fast Ethernet: UTP/STP Cat. 5, EIA/TIA-568 100-ohm, 100 meters max Gigabit Ethernet: UTP/STP Cat. 5, 5E, 6, EIA/TIA-568 100-ohm, 100 meters max Mini-GBIC: LC Type. 9/125μm or 10/125μm single-mode fiber optic cable (LX) LC Type. 62.5/125μm or 50/125μm multi-mode fiber optic cable (SX) |
| Console Port | RS-232, female 9-Pin Serial Port (M-M serial cable included) |
| Protocol/Topology | (CSMA/CD) / Star |
| Buffer Memory | 1Mb for Control, 3Mb for Packet Filter |
| Filtering Address Table | 6K MAC (255 entry of Static MAC), 4K VLAN and 2K Multicast Entries |
| LED Display | Power On(Green)/Off(Off) Diagnostic (Blinking) during Initialization Link(Green)/Activity(Blinking) Speed 100M(Green)/10M(Off) Gigabit Port: 1000Mbps(Green)/Activity(Blinking) |
| Power | Input: 100~240VAC, 50/60Hz Internal Power Supply |
| Power Consumption | 30 watts max. |
| Dimensions | 440 x 184 x 44mm (17.3 x 7.3 x 1.8 inch) (W x H x D) |
| Weight | 2.5 Kg. (5.2 lb.) |
| Temperature | Operating: 5( ~ 45( C (41( ~ 113( F) Storage: -20( ~ 70( C (-4( ~ 158( F) |
| Humidity | 10% ~ 90% non-condensing |
| Certifications/Safety | FCC, CE |

Packaging Contents			Related Products

- TEG-S2600i			- TEG-S2400i

- Quick Installation Guide		- TEG-S2500i

- CD-ROM (User’s Guide)

- Power Cord

- RS-232 Cable

- Rack Mount Kit

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

Sales: sales@trendware.com • Support: techsupport@trendware.com

Tech Support Hotline: (310) 626-6252

www.TRENDNET.com

# Text boxes

26-Port SNMP Stackable Switch

The TEG-S2600i 26 Port Stackable SNMP switch provides foundation for a highly scalable and easily managed network. The Web/SNMP Managed Switch allows network administrators to remotely monitor and manage network performance and security. Network administrators can stack up to 16 switches and manage them with a single IP address. The TEG-S2600i can be incorporated into high-speed backbone connectivity through Gigabit ports or mini-GBIC ports. Security and performance are optimized with advanced features including Port/Tag-based VLAN, QoS, and Trunking.

Front Panel

TEG-S2600i

Added Features

- 2 Pairs of Copper Gigabit port and Mini-GBIC slot