Features

- 3-Front Slot Supports Optional 10/100Mbps RJ45 or 100Base-Fiber modules.

- 1-Back Slot Supports Gigabit Copper or Fiber (SX/LX) modules

- IGMP (v1 and v2) Snooping Support for Multi-Media Application (up to 256 groups)

- Stack Management via One IP Address (up to 8 units), Easy Management by Web GUI

- Supports Port Bandwidth Control (per level 100k)

- Supports GVRP Function and Broadcast Storm Filter

- Supports Port Based VLAN, IEEE 802.1Q VLAN and IEEE 802.1v Protocol VLAN

- Supports Port Mirroring (max 25 entries) and Port Security

- Supports IEEE 802.3x Flow Control and IEEE 802.3ad Port Trunk with LACP (up to 7 groups, max 4 ports)

- Supports IEEE 802.1p Class of Service and IEEE 802.1d Spanning Tree Protocol

- Supports IEEE 802.1x User Authentication (Reject, Accept, Authorize, Disable)

- Store-and-Forward Switching Architecture with Non-Blocking Wire-Speed Performance

- Configuration via RS-232 Console Port, Telnet, SNMP and Web Browser (HTTP)

- Supports TFTP or Console Firmware Upgrade Feature

- 19” Rack Mount Design (kit included)

- 5-Year Warranty

Optional Modules (Not included)

| TEG-S3M8TX | 8-Port 10/100Mbps Auto-MDIX RJ-45 Port Module |
| --- | --- |
| TEG-S3M8FX | 8-Port 100Base-FX SC Type Multi-Mode Fiber Port Module |
| TEG-S3M8S15 | 8-Port 100Base-FX SC Type Single-Mode Fiber Port Module (15km) |
| TEG-S3M2CG | 2-Port 10/100/1000Mbps Auto-MDIX RJ45 Port Module |
| TEG-S3M2MG | 2-Slot 1000Base Mini-GBIC (SX/LX) Module for optional Mini-GBIC |
| TEG-S3M11CF | 1-Port Copper & 1-Port SX Fiber SC Type Multi-Mode Gigabit Port Module |

Specifications

| Hardware |
| --- |
| Standards | IEEE 802.3 10Base-T, IEEE 802.3u 100Base-TX/100Base-FX, IEEE 802.3z Gigabit SX/LX, IEEE 802.3ab Gigabit 1000T, IEEE 802.3x Flow Control and Back Pressure, IEEE 802.3ad Port Trunk with LCAP, IEEE 802.1d Spanning Tree Protocol, IEEE 802.1p Class of Service, IEEE 802.1Q VLAN Tagging |
| Optional Modules | TEG-S3M8TX : 8 x 10/100Mbps Auto-MDIX RJ45 Port TEG-S3M8FX : 8 x 100Base-FX SC type Multi-Mode Fiber Port TEG-S3M8S15 : 8 x 100Base-FX SC type Single-Mode Fiber Port (15km) TEG-S3M2CG : 2 x 10/100/1000Mbps Auto-MDIX RJ45 Port TEG-S3M2MG : 2 x 1000Base-FX Mini-GBIC Fiber Slot TEG-S3M11CF : 1 x Copper Gigabit, 1x 1000Base-FX SC Type Multi-Mode Fiber Port |
| Packet Forwarding and Filtering Rate | Gigabit: 1,488,000 packets per second per port 100M Ethernet: 148,800 packets per second per port 10M Ethernet: 14,880 packets per second per port |
| Cabling | RJ45: 10Base-T: 2 pairs UTP/STP Cat 3.4.5 cable EIA/TIA 568 100Ohm (100m) 100Base-T: 2 pairs UTP/STP Cat 3,4,5 cable EIA/TIA 568 100Ohm (100m) Gigabit: 4 pairs UTP/STP Cat 5, 5e, 6 cable EIA/TIA 568 100Ohm (100m) Multi-Mode: (50/125um, 62.5/125um), 2km (max) Single-Mode: (8/125um, 10/125um) |
| Console Port | RS-232, female 9-Pin Serial Port (M-M serial cable included) |
| Protocol/Topology | (CSMA/CD) / Star |
| Buffer Memory | 3Mbits Data Buffer |
| Filtering Address Table | 8K MAC Address Entries |
| Bandwidth | Up to 8.8Gbps |
| LED Display | Power 10/100Mbps-TX: Link/Activity, Full Duplex 100Base-FX: Link, Activity Gigabit Copper: Link/Activity, Full Duplex, 1000Mbps, 100Mbps Gigabit Fiber: Link/Activity |
| Power | Input: 100~240VAC, 50/60Hz, 0.8A Internal Power Supply |
| Power Consumption | 60 watts |
| Dimensions | 440 x 280 x 44mm (17.3 x 11 x 1.7 inch) (W x H x D) |
| Weight | 5.1 Kg. (11 lb.) |
| Temperature | Operating: -10( ~ 60( C (14( ~ 140( F) Storage: -40( ~ 70( C (-40( ~ 158( F) |
| Humidity | 10% ~ 90% non-condensing |
| Safety Emissions | FCC, CE |
| Software |
| Management | Web Management, RS-232 Console Management, Telnet |
| RFC Standard | RFC 1157 SNMP, RFC 1213 MIB II, RFC 1643 Ethernet like, RFC 1493 Bridge MIG, RFC 1757 RMON 1, RFC 1215 Trap, RFC 2674 VLAN MIB, Private MIB |
| SNMP Trap | Cold Start, Link Down, Link Up, Authorization Fail, Fan Fail Trap Trap Station up to 3 |
| VLAN | Static VLAN up to 256 groups, Dynamic VLAN up to 2048 groups, VLAN ID 0~4094 |
| QoS Policy | 8 Priority Levels ID for 2 Priority Queue |
| Class of Service | High/Low Queue. Service Rule: FCFS, High before Low, WRR for High or Low Weight |

Packaging Contents			Related Products

- TEG-S3000i			- TEG-S3M8TX		- TEG-S3M2CG

- Quick Installation Guide		- TEG-S3M8FX		- TEG-S3M2MG

- Power Cord				- TEG-S3M8S15	- TEG-S3M11CF

- CD-ROM (User’s Guide)

- RS-232 Cable / Rack Mount Kit

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

Sales: sales@trendnet.com • Support: techsupport@trendnet.com

Tech Support Hotline: (888)777-1550

www.trendnet.com

# Text boxes

4-Slot Gigabit Layer 2 Managed Chassis

The 4-Slot Gigabit Layer 2 Managed Chassis offers a cost-effective solution for an enterprise backbone network.  With 3 line card slots and a wide range of hot-swappable modules, the switch provides an easy scalable expansion as your needs grow. Features include port trunking, load balancing, SNMP, IGMP, VLAN, Virtual Cable testing, and other network management features.

TEG-S3000i