FEATURES

- Supports 32-bit PCI Local Bus Rev. 2.2

- Provides drivers supporting Windows 98(SE)/ME/2000/XP

- Uses 2.4 GHz frequency band, which complies with worldwide requirement

- Delivers data rate up to 22Mbps

- Dynamically shifts between 22, 11, 5.5, 2 and 1Mbps network speed (based on signal strength), for maximum availability and reliability of connection

- Supports Ad-Hoc mode (peer-to-peer) and Infrastructure mode (with Access Point) wireless network architecture

- Roaming feature allows users to move between Access Points without loosing their connection

- Ensures optimal security by providing 64/128/256-bit Wired Equivalent Privacy (WEP) encryption as defined in the IEEE 802.11b standard

- Detachable antenna with Reverse SMA connecter

- Distance coverage 30 to100 meters indoor, 100 to 300 meters outdoors

- 3-year Warranty

TREND SPEC’S

Adapter Type:	32-bit PCI Bus

Standards:	IEEE 802.11b, Wi-Fi, and PCI Local Bus Rev. 2.2

Frequency:	2.4 ~ 2.4835GHz (Industrial Scientific Medical Band)

Channels:	11 Channels (US & Canada)

Data Rate:	22Mbps, 11Mbps, 5.5Mbps, 2Mbps, 1Mbps

Modulation Technology:	Direct Sequence Spread Spectrum (DSSS), PBCC (Packet Binary Convolutional Coding), 11-chip Barker Sequence

Antenna (External):	Detachable 2dBi Antenna (length = 103 mm) with Reverse SMA connector

Media Access Protocol:	CSMA/CA with ACK

LED Indicator:	Power

Output Power:	16 ~ 18dBm (typical)

Receiving Sensitivity:	-80dBm (typical)

Power Consumption:	DC +3.3V. TX: 650mA (max.)

Dimensions:	134 x 120 x 24 mm (5.28 x 4.72 x 0.94 inch) (without the antenna)

Weight:	65 g. (2.3 oz.)

Operating Temperature:	0( ~ 55( C (32( ~ 131( F)

Storage Temperature:	-20( ~ 70( C (-4( ~ 158( F)

Humidity:	Max. 95% (Non-condensing)

Certification:	CE, FCC

TOP REASONS THE TEW-303PI IS A LASTING TREND

Integration Friendly:	Drivers support Windows 98/ME/2000/XP.

Economical:	Save time, labor, and material for network cable installation.

Flexible:	Creates wireless peer-to-peer network in Ad-Hoc mode or connects to Ethernet LAN in Infrastructure mode using wireless Access Point.

Security:	Supports 256-bit Wired Equivalent Privacy (WEP) encryption.

Performance:		Connects at a speed up to 22Mbps, which is two times faster than regular 802.11b products.

TEW-301PC		11/22Mbps Wireless PC Network Adapter for Notebook

TEW-302CF		11/22Mbps Wireless CompactFlash Network Adapter

TEW-303PI		11/22Mbps Wireless PCI Network Adapter

TEW-304UB		11/22Mbps Wireless USB Network Adapter

TEW-310APB		11/22Mbps Wireless Access Point + Bridge

TEW-311BRP		11/22Mbps Wireless AP Router with 4-Port Switch

TEW-PS3		3-parallel port Wireless Ethernet Print Server

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

## Sales: sales@trendware.com • Support: techsupport@trendware.com

# Text boxes

Product Information

#### TEW-303PI

### 11/22Mbps Wireless PCI Network Adapter

TRENDnet’s TEW-303PI 11/22Mbps Wireless LAN PCI Card creates freedom for your desktop PC.  This PCI Card plugs right into your PCI bus slot providing wire-free access to networked resources from your LAN (Local Area Network) and Internet or create a network without networking cables.  It dynamically shifts between 22, 11, 5.5, 2, and 1 Mbps for maximum availability and reliability.  Complying with 2.4 GHz frequency band and IEEE 802.11b standard, TRENDnet’s TEW-303PI ensures optimal security and performance for your wireless networking environment.

11/22Mbps Wireless Network Solution