FEATURES

- Operates as Access Point, Wireless Bridge, or Access Point Client

- Uses 2.4GHz frequency band, which complies with worldwide requirement

- Direct Sequence Spread Spectrum (DSSS) wireless technology

- 10/100Mbps auto-sense Fast Ethernet port

- Provides data rate bandwidth up to 22Mbps with automatic fallback

- Easy configuration with Web Browser and Windows Configuration Software

- DHCP Server supports up to 100 clients

- Provides 64/128/256-bit Wired Equivalent Privacy (WEP) encryption

- Access Control with wireless client’s MAC Address

- Detachable 2dBi Dual Dipole Antennas. Replace either one with optional High-Gain antenna to extend the range/coverage area.

- Wall-Mountable

- Distance coverage 35 to100 meters indoor, 100 to 300 meters outdoors

- 3-Year Warranty

TREND SPEC’S

### Wireless LAN Interface

Standards: 		IEEE 802.11b Wireless LAN

Modulation Technology:	Direct Sequence Spread Spectrum (DSSS), PBCC (Packet Binary Convolutional Coding), 11-chip Barker Sequence

Channels:	11 Channels (US & Canada)

Data Rate:	22Mbps, 11Mbps, 5.5Mbps, 2Mbps, and 1Mbps (auto-fallback)

Operating Mode:	AP, AP-to-AP, AP-to-Multiple AP, or AP Client

Frequency Range:	2.4 ~ 2.4835 GHz

Security:	64/128/256-bit WEP Encryption

Antenna:	2 x 2dBi Detachable Dipole Antenna with female Reverse SMA connector

(90° elbow, Length = 137 mm / 5.39 inches)

Output Power:	16 ~ 18 dBm (max.)

Receiving Sensitivity:	- 82 dBm (Typical)

#### Wired LAN Interface

Standards:	IEEE 802.3 (10Base-T) and IEEE 802.3u (100Base-TX)

Data Rate Transmission:	10/100Mbps, Half/Full duplex auto-negotiation

Media Connector:	1 x UTP/STP RJ-45

Cabling: 	Cat. 5 UTP/STP RJ-45 Cable (100 meters max.)

LED Indicators:	Power, TX/RX, Link

Power:	External Power Adapter, Input: 100~240VAC, 1A, 50~60Hz. Output: 5VDC, 2A

Dimensions:	140 x 113 x 38 mm (5.51 x 4.45 x 1.5 inches) (antenna folded)

Weight:	213 g. (7.5 Oz.)

Temperature:	Operating: -10( ~ 55(C (14(F ~ 131(F); Storage: -20( ~ 65(C (-4(F ~ 149(F)

Humidity:	Max. 95% (non-condensing)

Certification:	CE, FCC Class B

TOP REASONS THE TEW-310APBX IS A LASTING TREND

Integration Friendly:	Supports both Ethernet and Fast Ethernet, with Web Browser configuration for fast and easy setup.

Economical:	Attaches to Ethernet network at anytime to add wireless users on the network. Save time, labor, and material for network cable installation.

Flexible:	Works as stand-alone Access Point, Single/Multiple Access Point(s) Bridge, or Ethernet Access Point Client.

Security:	Provides 64/128/256-bit WEP Encryption and MAC Address Access Control.

Cost Effective:		One unit provides multiple wireless connections to wired LAN.

TEW-310APBX	11/22Mbps Wireless Access Point + Bridge with Detachable Antennas

TEW-310APB	11/22Mbps Wireless Access Point + Bridge

TEW-311BRP	11/22Mbps Wireless AP Router with 4-Port Switch

TEW-PS3		3-port Wireless Ethernet Print Server

TEW-IA04O	4dBi Omni Antenna (indoor) for IEEE 802.11b 2.4GHz ISM Band

TEW-IA06D	6dBi Directional Antenna (indoor) for IEEE 802.11b 2.4GHz ISM Band

TEW-OA14DK	14dBi Directional Antenna (outdoor) for IEEE 802.11b 2.4 GHz ISM Band with Mounting Hardware and 2 Meters Antenna Cable (TEW-2000F; Female N-Type and Female Reverse SMA Connectors)

##### To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

## Sales: sales@trendware.com • Support: techsupport@trendware.com	ss10272003

# Text boxes

11/22Mbps Wireless Access Point + Bridge with Detachable Antennas

TRENDnet’s TEW-310APBX Wireless Access Point is today’s link to Wireless Technology.  Compliant with the IEEE Wireless Networking Standard 802.11b, it provides Direct Sequence Spread Spectrum (DSSS) operation for transparent bridging and roaming capabilities for wireless nodes. The TEW-310APBX also provides AP-to-AP bridging functions, allowing users to connect two or more Access Points together, wirelessly.  With TRENDnet’s Wireless Access Point and Wireless Network Adapters, users can connect to Ethernet/Fast Ethernet LAN at home or office to access network resources such as hard drives, CD-ROM/DVD drives, network printers, and Internet connection - with coverage up to 300 meters.

TEW-310APBX

11/22Mbps Wireless Network Solution

Product Information