FEATURES

- Uses 2.4 GHz frequency band (DSSS), which complies with worldwide requirements

- Supports IEEE 802.11g or 802.11b (11Mbps) wireless devices

- Dynamic data rate shift at 54, 48, 36, 24, 18, 12, 9 and 6Mbps for 802.11g

- Dynamic data rate shift at 11, 5.5, 2 and 1Mbps for 802.11b

- Supports Ad-Hoc (peer-to-peer) mode and Infrastructure mode (Access Point)

- Compatible with Windows 98(SE)/ME/2000/XP

- Supports 64/128-bit Wired Equivalent Privacy (WEP)

- Supports Wireless Fidelity Protected Access (WPA)

- Low interference and High susceptibility guarantee reliable performance

- 2dBi antenna with Integrated Microstrip Dual Diversity Antenna

- Distance Coverage 35~100 meters indoor, 100~300 meters outdoor (depending on the environment)

- Simple User Setup & Diagnostics Utilities

- 3-Year Warranty

TREND SPEC’S

Interface Type:		CardBus Type II specification 32-bit data bus

Standards:		IEEE 802.11b and IEEE 802.11g

Antenna:		2dBi Integrated Microstrip Dual Diversity Antenna

Data Rate (auto fallback):		802.11b: 11Mbps, 5.5Mbps, 2Mbps, and 1Mbps

802.11g: 54Mbps, 48Mbps, 36Mbps, 24Mbps, 18Mbps, 12Mbps, 9Mbps and 6Mbps

Module Technique:			802.11b: CCK (11 and 5.5Mbps), DQPSK (2Mbps), DBPSK (1Mbps)

802.11g: OFDM

Media Access Protocol:		CSMA/CA with ACK

Frequency:		2.4 to 2.497 GHz (Industrial Scientific Medical Band)

LED Indicator:		Power, Link

Output Power:		15dBm (typically) @ 802.11b

12dBm (typically) @ 802.11g

Receiving Sensitivity:		54Mbps 10 – 5 BER @ -73 dBm (typical)

22Mbps 10 – 5 BER @ -85 dBm (typical)

11Mbps 10 – 5  BER @ -86 dBm (typical)

Encryption:			64/128-bit

Support OS:			Windows 98(SE), ME, 2000, XP

Channels:		        1~11 channels (FCC), 1~13 channels (ETSI), 1~14 channels (MKK-Japan),

10~13 channels (France), 3~9 channels (Israel)

Power Consumption:		Receive Mode: 480mA

Transmit Mode: 650 mA

Dimensions (LxWxH):		118 x  54 x  7 mm (4.65 x 2.1 x 0.2 inches)

Weight:		36 g ( 1.27 oz.)

Operating Temperature:			0( ~ 40( C (32( ~ 104( F)

Storage Temperature:			-20( ~ 70( C (-4( ~ 158( F)

Humidity:			10% ~  95% max. (Non-condensing)

Certification:			FCC, CE, ETS

##### TOP REASONS THE TEW-421PC IS A LASTING TREND

Economical:	Save time, labor, and materials; compare with wired network installation.

Flexible:	Creates wireless peer-to-peer network in Ad-Hoc mode or connects to Ethernet LAN in Infrastructure mode using Wireless Access Point or Wireless Router.

Cost Effective:	Supports IEEE 802.11b and IEEE 802.11g standards; connects to any IEEE 802.11b and 802.11g wireless network.

Performance:	54Mbps high-speed wireless connection.

TEW-421PC	54Mbps 802.11g Wireless PC Card

TEW-423PI	54Mbps 802.11g Wireless PCI Network Adapter

TEW-410APB	54Mbps Wireless Access Point + Bridge

TEW-431BRP	54Mbps 802.11g Wireless Router

TEW-IA04O	4dBi Indoor Omni Antenna

TEW-IA06D	6dBi Indoor Directional Antenna

TEW-OA08OK	8dBi Outdoor Omni Directional Antenna

TEW-OA14DK	14dBi Outdoor Directional Antenna

TEW-OA24D	24dBi Outdoor Directional Parabolic Antenna

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

## Sales: sales@trendware.com • Support: techsupport@trendware.com

# Text boxes

### 54Mbps 802.11g Wireless PC Card

TRENDnet's TEW-421PC 54Mbps Wireless CardBus PC Card allows laptop users the mobile freedom to connect at home, in the office or to wireless hotspots on the road. It complies with the IEEE 802.11g standard, making it backward compatible with 802.11b networks for assured compatibility as you roam between networks. Advanced Wi-Fi Protected Access (WPA) and up to 256-bit WEP encryption are supported to provide secure access for your data. Cut the wires and move freely with TRENDnet’s 802.11g wireless products.

#### TEW-421PC

Product Information

IEEE 802.11g Wireless Network Solution