Features

- Wi-Fi Compliant with IEEE 802.11g and IEEE 802.11b Standards

- Uses 2.4 GHz Frequency Band, which Complies with Worldwide Requirements

- Supports Ad-Hoc (Peer-to-Peer) Mode or Infrastructure (AP-Client) Mode

- Dynamic Data Rate Scaling at 54, 48, 36, 24, 18, 12, 9 and 6Mbps for 802.11g

- Dynamic Data Rate Scaling at 11, 5.5, 2 and 1Mbps for 802.11b

- Maximum Reliability, Throughput and Connectivity with Automatic Data Rate Switching

- Compatible with Windows 98SE/ME/2000/XP

- Supports 64/128-bit WEP, WPA/WPA2 and WPA-PSK/WPA2-PSK

- Detachable 2dBi dipole Antenna with Reverse SMA Connector

- Low Interference and High Susceptibility Guarantee Reliable Performance

- Range of 35~100 meters indoor, 100~300 meters outdoor (depends on the environment)

- Simple User Setup & Diagnostics Utilities

- 3-Year Warranty

Specifications

| Hardware |
| --- |
| Interface | 32-bit PCI 2.2 Bus Master |
| Standards | IEEE 802.11b and IEEE 802.11g |
| Antenna | 1 x 2dBi Detachable Dipole Antenna |
| LED Indicator | Link |
| Power Consumption | Receive Mode: 370mA Transmit Mode: 470 mA |
| Supported OS | Windows 98, ME, 2000, XP |
| Dimensions (LxWxH) | 121 x 44 mm (4.8 x 1.7 inches) (without metal bracket) |
| Weight | 60g (2.1oz.) (with antenna) |
| Temperature | Operating: 0( ~ 40( C (32( ~ 104( F) Storage: -10( ~ 70( C (14( ~ 158( F) |
| Humidity | 10% ~ 95% max. (Non-condensing) |
| Emissions | FCC, CE |
| Wireless |
| Module Technique | 802.11b: CCK (11 and 5.5Mbps), DQPSK (2Mbps), DBPSK (1Mbps) 802.11g: OFDM |
| Frequency | 2.412 to 2.484 GHz (Industrial Scientific Medical Band) |
| Media Access Protocol | CSMA/CA with ACK |
| Data Rate (auto fallback) | 802.11b: 11Mbps, 5.5Mbps, 2Mbps, and 1Mbps 802.11g: 54Mbps, 48Mbps, 36Mbps, 24Mbps, 18Mbps, 12Mbps, 9Mbps and 6Mbps |
| Output Power | 15dBm (typical) @ 802.11b 13dBm (typical) @ 802.11g |
| Receiving Sensitivity | 54Mbps 10% PER @ -72 dBm (typical) 11Mbps 8% PER @ -85 dBm (typical) |
| Security | WPA/WPA2(TKIP), WPA-PSK/WPA2-PSK(AES/TKIP), 64/128-Bit WEP (Hex or ASCII) |
| Channels | 1~13 Channels (Universal Domain Support) |

Related Products				Package Contents

- TEW-421PC					- TEW-423PI

- TEW-424UB					- Utility & Driver CD-ROM

- TEW-432BRP					- Multi-Language Quick Installation Guide

To order please call: 888-326-6061

20675 Manhantta Place, CA 90501 • (310) 961-5500 • Fax: (310) 961-5511

## Sales: sales@trendnet.com • Support: support@trendnet.com

## Tech Support Hotline: (866)845-3673

Official Site: www.TRENDnet.com

# Text boxes

### 54Mbps 802.11g Wireless PCI Adapter

TEW-423PI 54Mbps Wireless PCI Card cuts the wires to your desktop and provides 54Mbps speed to handle bandwidth-intensive applications. It complies with the IEEE 802.11g standard, making it backward compatible with 802.11b networks for assured compatibility. Advanced 128-bit WEP encryption is supported to provide secure access for your data. Cut the wires and move your desktop where you need it with TRENDnet’s 802.11g wireless PCI Card.

#### TEW-423PI (c1.0R)

New Implements

- New Chipset

- Receiving Sensitivity Change