Features

- Wi-Fi Compliant with IEEE 802.11g and IEEE 802.11b Standards

- Detects IEEE 802.11b, and 802.11g HotSpots and Connects to IEEE 802.11b or 802.11g Wi-Fi Devices

- 512MB Flash Memory Drive with 9MB/s read and 8MB/s write speed performance

- Auto-install Loads Driver and Utility from the Flash Drive Automatically

- Supports Ad-Hoc (Peer-to-Peer) Mode or Infrastructure (AP-Client) Mode

- Dynamic Data Rate Scaling at 54, 48, 36, 24, 18, 12, 9 and 6Mbps for 802.11g

- Dynamic Data Rate Scaling at 11, 5.5, 2 and 1Mbps for 802.11b

- Built-in Rechargeable Li-on Battery (Automatically charge when connected to the USB port)

- Hotspot Finder displays SSID, Channel, Encryption Types and Signal Strength information

- Maximum Reliability, Throughput and Connectivity with Automatic Data Rate Switching

- Supports 64/128-bit WEP, WPA/WPA2 and WPA-PSK/WPA2-PSK without Performance Degradation

- Low Interference and High Susceptibility Guarantee Reliable Performance

- Wireless Function Compatible with Windows 98SE/ME2000/XP (SP1/SP2)/2003 Server

- Range of 35~100 meters indoor, 100~300 meters outdoor (depends on the environment)

- Simple Plug & Play  Installation, No CD Required & Diagnostics Utilities

- 3-Year Warranty

Specifications

| Hardware |
| --- |
| Interface | USB 2.0, 1.1 Compliant |
| LCD / LED | 96 x 32 pixels / PWR, ACT |
| Control | Power On/Off, Scan, Next |
| Rechargable Battery | 180mAh |
| Power Consumption | 280mA |
| Dimensions (LxWxH) | 97.3 x 28.6 x 14 mm (3.8 x 1.1 x 0.6 inches) |
| Weight | 35g (1.2 oz.) |
| Temperature | Operating: 0( ~ 40( C (32( ~ 104( F) Storage: -20( ~ 70( C (-4( ~ 158( F) |
| Humidity | 10% ~ 90%max (Non-condensing) |
| Safety Emissions | FCC, CE |
| Wireless |
| Module Technique | 802.11b: CCK (11 and 5.5Mbps), DQPSK (2Mbps), DBPSK (1Mbps) 802.11g: OFDM |
| Frequency | 2.412 ~ 2.484 GHz |
| Media Access Protocol | CSMA/CA |
| Compatible OS | Windows 98SE/ME2000/XP (SP1/SP2)/2003 Server |
| Data Rate (auto fallback) | 802.11b: 11Mbps, 5.5Mbps, 2Mbps, and 1Mbps 802.11g: 54Mbps, 48Mbps, 36Mbps, 24Mbps, 18Mbps, 12Mbps, 9Mbps and 6Mbps |
| Transmit Power | 802.11b: 18dBm @ 11Mbps / 802.11g: 15dBm @ 54Mbps |
| Receiving Sensitivity | 802.11b: 11Mbps 10 – 5 BER @ -87dBm 802.11g: 54Mbps 10 – 5 BER @ -72dBm |
| Encryption | 64/128-bit WEP (Hex or ASCII), WPA/WPA2, and WPA-PSK/WPA2-PSK |
| Channels | US: 1~11, EU: 1~14 |
| Flash Drive |
| Compatible OS | No Driver Required: Windows ME/2000/XP/2003, Mac OS 9.x +, Linux 2.4 + Driver Required: Windows 98/98SE |

Package Contents				Related Products

- TEW-429UF					- TEW-421PC

- User’s Guide CD-ROM				- TEW-423PI

- Multi-Language Quick Installation Guide	- TEW-430APB

- USB 2.0 Cable (15cm)	/Neck Strap		- TEW-432BRP

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

## Sales: sales@trendware.com • Support: techsupport@trendware.com

Tech Support Hotline: (310)626-6252

Official Site: www.trendnet.com

# Text boxes

HotFlash 802.11g Wireless & 512MB Flash Memory

Combo USB Adapter with HotSpot Detector

The 802.11g Wireless & 512MB Flash Memory Combo USB Adapter with HotSpot Detector incorporates a Wi-Fi Detector, a wireless adapter, and a USB flash drive into an all-in-one mobile solution.  Scan nearby hotspots and view site survey information with the built-in LCD.  Store files such as business presentations, family photos, or other important documents.

#### TEW-429UF

* Please note: Some of the listed capacity is used for formatting and other functions (20MB is reserved for User’s Guide and Driver Utility) and thus is not available for data storage. Please see User’s Guide for detail.