FEATURES

- IEEE 802.11g 54Mbps and IEEE 802.11b 11Mbps Wireless Standards Compliant

- Supports most operating systems, such as Windows 95/98/ME/NT/2000/XP, Unix, and Mac

- Compliant with ITU-T G.dmt, G.lite and multi-mode for ADSL modems

- Support PPPoE, PPPoA and IPoA

- 2dBi Detachable Antenna with Reverse SMA Connector

- High Speed Wireless Connection up to 54Mbps with automatic fallback

- 64/128-bit Wired Equivalent Privacy (WEP)

- Built-in 4 Port 10/100Mbps Auto-Sensing and Auto-MDIX Switch

- Web Access Control using URL Keywords, Time/Date and Services Type

- Supports Virtual DMZ, Virtual Servers (Port Forwarding) and Firewall Rules

- Supports RIP/Static Routing and Dynamic DNS Service

- Supports 100 sessions of VPN Pass-Through for PPTP, IPSec and L2TP

- NAT/NAPT Firewall and Stateful Packet Inspection (SPI) protects against Dos attack

- Real-Time email alert and logs when attack/unauthorized Internet activity occurs

- DHCP Server feature supports up to 253 Users

- Supports UPnP (Universal Plug & Play) and ALGs Support Internet applications such as Email, FTP, Gaming, ICQ,

Net Meeting, PING, Telnet, and more

- Easy Configuration and Remote Management with Web Browser (HTTP)

- Flash memory for firmware upgrade

- 3-Year Warranty

TREND SPEC’S

### Standards: 	            IEEE 802.3 (10Base-T), and IEEE 802.3u (100Base-TX), IEEE 802.11b (11Mbps) and IEEE 802.11g

Protocols:                          NAT/NAPT, PPPoE & PPPoA, HTTP, DHCP, TCP/IP &UDP, PAP&CHAP, RIP1, DDNS, UPnP

Firewall:	NAT firewall, Rule-Based Policy Firewall, Attack Alert (email) and log, Stateful Packet Inspection firewall for DoS (Denial of Service) Attacks

Module Technique:	802.11b: CCK, DQPSK, DBPSK	802.11g: OFDM

Data Rate (auto fallback): 	802.11b: 11Mbps, 5.5Mbps, 2Mbps, and 1Mbps

802.11g: 54Mbps, 48Mbps, 36Mbps, 24Mbps, 18Mbps, 12Mbps, 9Mbps and 6Mbps

Frequency Range:	2.4 ~ 2.497 GHz

Channels:	11 Channels (US)

Security:	64/128/256-bit (WEP)

Antenna:	1 x 2dBi External Detachable Dipole Antenna with Female Reverse SMA Connector

Output Power:	15 dBm ( 1dBm

Receiving Sensitivity:	11Mbps 10 – 5 BER @ -80 dBm (typical); 54Mbps 10 – 5 BER @ -65 dBm (typical)

ATM:                                   Support AAL5 (optional AAL 2), UBR (optional CBR, VBR), VPI Range (0 ~ 255) and

VCI range (1 ~ 65535), 1 PVC, OAM F4/F5 loop back.

Payload Encapsulation.

RFC2684 (RFC1483) Multi-Protocol over ATM; RFC2225 (RFC1577) IPoA;

RFC2364 PPP over ATM (CHAP&PAP); RFC2516 PPPoE over ATM

LAN Port:                           4x 10/100Mbps Ethernet port (RJ-45), Auto-MDIX

WAN Port:	Compliant to G.dmt (G.922.1) Annex A; Compliant to G.lite (G.922.2) and T1.413 Annex A

ADSL Line Interface (RJ-11); Line Impedance: 100 Ω

LEDs:                                  Power, Status, 10/100 (LAN 1~4), WAN, WLAN

Power:	15V DC, 1A. External Power Adapter

Dimensions (LxWxH):	183 x 125 x 31 mm (7.2 x 4.9 x 1.2 inches)

Unit Weight:	Appr. 408 g  (0.9 lb)

Temperature:                     Operating: 0˚  ~ 40˚ C (32˚ ~ 104˚ F) 	Storage: -20˚ ~ 70˚ C (-4˚ ~ 158˚ F)

Humidity:	Operating: 10 ~ 90% RH 		Storage: 5 ~ 95% RH

Certification:	FCC, CE

### TOP REASONS THE TEW-435BRP IS THE LASTING TREND

Easy Integration: ADSL Modem, Internet Router, Wireless Access Point, and 4-port 10/100Mbps Switch all in one unit. Share your broadband Internet connection with 802.11g/802.11b wireless and wired Ethernet clients.

Cost-Effectiveness: Saves on network cable installation fee and on-line charges.

Security: NAT & SPI firewall protection keeps hackers out. 64/128-bit WEP protect Access Point from unwanted wireless clients.

Traffic Control: Controls network traffics with Access Control, DMZ and Virtual Server.

Performance: Share your high-speed Internet access with wireless connection speed up to 54Mbps.

TEW-435BRM	802.11g 54Mbps ADSL Firewall Router

TEW-421PC	54Mbps 802.11g Wireless PC Card

TEW-403PI	54Mbps 802.11g Wireless PCI Adapter

TEW-IA04O	4dBi Omni Directional Indoor Antenna

TEW-IA06D	6dBi Directional Indoor Antenna

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

Sales: sales@trendware.com • Support: techsupport@trendware.com

www.TRENDNET.com

# Text boxes

802.11g 54Mbps ADSL Firewall Router

TRENDnet’s TEW-435BRM delivers the most complete high-performance network combined ALL-IN-ONE box. It is ideal for home or small offices looking for a secure, flexible, high-performance wireless network that is easy to install. It includes a Wireless 802.11g 54Mbps Access Point, ADSL Modem, SPI Firewall, Router, and 4-Port Switch. Advanced security includes a Stateful Packet Inspection (SPI) and Rule-Based Firewall, while the Application Level Gateway (ALG), DMZ and Port Forwarding features add flexibility so designated programs such as gaming and web-conferencing programs can work easily behind the Firewall. Control user Internet access via URL, time, and MAC address, while Logs and reports provide monitoring of intrusion attempts and traffic. Set-up is easy with UPnP support and web browser based Quick Install Wizard.

Network Solution

for TEW-435BRM

TEW-435BRM

Product Information